## Slide 1
VIRGINIA ADVANCED SHIPBUILDING & CARRIER INTEGRATION CENTER
John Boyle
Structural Option
Thesis Advisor – Dr. Behr
NEWPORT NEWS, VA
Source: Clark-Nexsen
Source: Clark-Nexsen

## Slide 2
ACKNOWLEDGEMENTS
I would like to thank the following individuals for their support on this project
Professor M. Kevin Parfitt
Professor Robert Holland
Dr. Behr
Kurt J. Clemente
I would also like to thank my parents, John and Diana for their relentless support throughout this semester

## Slide 3
Introduction
  Building Statistics
  Architecture
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Building Statistics
Building Occupancy Name: Northrop Grunman Newport News
Occupancy Type: Office / Research / Shipbuilding Facility
Size: 241,000 sf
Number of Stories: 8
Date of Construction: December 1999-February 2002
Actual cost: $58 million
Project Delivery: Design-Bid-Build
Project Team
Clark-Nexsen Architecture & Engineering
Source: Clark-Nexsen

## Slide 4
Architecture
Achieves light, open feel
  Uses steel wide-flange members
  Enclosed in reflective curtain wall
Curve shape
  Gives appearance of a tall, glass ship looking over the James River
Concrete “figurehead”
Introduction
  Building Statistics
  Architecture
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Source: Clark-Nexsen

## Slide 5
Existing Structural System
Wide-flange steel column on a concrete pedestal
  Placed around perimeter of the building
Soil Condition: Unstable soil
Grade beams: 20” & 22”
  Resist lateral column base movement
  Distribute weight of the building over soil
FOUNDATION
CONC. PEDESTAL PLAN
CONC. PEDESTAL SECTION
Introduction
Existing Structural System
  Foundation
  Gravity
  Lateral
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Source: Clark-Nexsen
Source: Clark-Nexsen
Source: Clark-Nexsen
Notes: Unstable Soil due to waterfront location of building
Grade beams important due to unstable soil conditions
22” – Blue
20” - Red

## Slide 6
Existing Structural system
FLOOR
  4.5” total thickness composite steel deck and slab
    Lightweight concrete placed 2” deep, .038” thick galvanized steel deck
    Yield Strength: 33 ksi
BEAMS / COLUMNS
  Steel wide-wide flange members
  W12x14 – W18x40 used for beams
  W8, W10, W12, W14 used for columns
1st Floor
  5” slab on grade w/ 6x6 W2.9xW2.9 WWF (blue)
  8” slab on grade- #4 bars @ 12” o.c. (red)
  6” slab on grade w/ 6x6 W2.9xW2.9 WWF (green)
GRAVITY
Floors 2-7
Structural Floorplan
First Floor
Structural Floorplan
Introduction
Existing Structural System
  Foundation
  Gravity
  Lateral
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Source: Clark-Nexsen
Source: Clark-Nexsen

## Slide 7
Existing Structural System
LATERAL
K-Braced Frame
  Wide-flange members used for vertical members
    W14x82 – W14x90 – W14x159
  HSS members used for cross-bracing
X-Bracing used in 3 bays
  Penthouse resists largest wind force
  Bays on bottom level have added weight of floors above
  X-bracing allows one member to be in tension and one to be in compression
Caters well to the shape of the building
Allows lateral loads to be distributed throughout the unique shape of the building
K-Braced Frame Location
K-Braced Frame Section
Introduction
Existing Structural System
  Foundation
  Gravity
  Lateral
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Source: Clark-Nexsen
Source: Clark-Nexsen
Notes: W14x82 at top
W14x90 in middle
W14x159 bottom

## Slide 8
Problem Statement
Curved shape leads to confusing column layouts
Current column layout leads to confusing beam and joist layouts
Creates great differences in floor depth
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 9
Problem Solution
Investigate new column layouts
Redesign structural system using reinforced concrete
  Composite Steel Deck / Wide flange steel beams
    => Two-way flat slabs
  Wide flange steel columns
    => Reinforced concrete columns
  K-Braced lateral resisting frame
    => Shear walls
Reduces floor thickness which will allow building to keep a light, open feel and may reduce cost
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 10
Architectural Breadth:
Column Layout Redesign
Current Column Layout
Redesigned Column Layout
Original column layout:
  Contains irregularly shaped bays
  Crafted to shape of building
Redesign
  Created grid using existing perimeter columns
  Created moderately sized, rectangular bays
  Will make designing column strips and drop panels easier
  Smallest Bay: 24’-11” x 2’-3”
  Largest Bay: 29’-11” x 33’-10”
  Columns are placed with little-to-no interference with the current floor plan
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Source: Clark-Nexsen
Source: Clark-Nexsen

## Slide 11
Architectural Breadth:
Column Layout Redesign
Current Column Layout
Redesigned Column Layout
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Original column layout:
  Contains irregularly shaped bays
  Crafted to shape of building
Redesign
  Created grid using existing perimeter columns
  Created moderately sized, rectangular bays
  Will make designing column strips and drop panels easier
  Smallest Bay: 24’-11” x 2’-3”
  Largest Bay: 29’-11” x 33’-10”
  Columns are placed with little-to-no interference with the current floor plan

## Slide 12
Slab Redesign
Original floor system
  Composite steel deck
  Wide-flange steel beams
  Floor thickness: 22.5”
Redesign
  Two-way flat slab: 4,000 psi concrete
  Advantages
    Easy formwork
    Simple bar placements
    Minimize floor-to-floor heights
Results
  12” thickness w/ 3” drop panels
  Penthouse:
    10” thickness w/ 3” drop panels
  Nearly 8”/floor reduction
SLAB THICKNESS FLOORS 1-7
SLAB THICKNESS PENTHOUSE
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
  Results
  Architectural Impact
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 13
Slab Redesign
Architectural Impact
  8” reduction in floor thickness
  Reduces total floor height by nearly 5 feet
FLOOR | HEIGHT (CURRENT BUILDING) | HEIGHT (REDESIGN)
1st | 0’-0” | 0’-0”
2nd | 17’-6” | 17’-6”
3rd | 32’-10” | 32’-2”
4th | 47’-2” | 45’-10”
5th | 61’-6” | 59’-6”
6th | 75’-10” | 73’-2”
7th | 90’-2” | 86’-10”
Penthouse | 104’-6” | 99’-8”
Roof | 126’-3” | 122’-1”
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
  Results
  Architectural Impact
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 14
Loads
Live loads
Dead loads
OCCUPANCY | DESIGN LOAD (psf) | THESIS LOAD (psf)
Penthouse Roof | 20 | 20
Low Roof | 80 | 60
Penthouse Floor | 125 | 125
Offices | 80 | 50
Conference Rooms | 100 | 100
Corridors | 100 | 80
Stairs | 100 | 100
Toilets | 75 | 75
LOAD TYPE | LOAD
Normal Weight Concrete | 150 pcf
Lightweight Concrete | 120pcf
MEP | 10psf
Partitions | 20psf
Finishes | 10psf
Curtain Wall | 15psf
GRAVITY
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
  Gravity
  Wind
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis
Source: Clark-Nexsen
Source: Clark-Nexsen

## Slide 15
Loads
WIND
Location: Newport News, VA
Exposure: D (Building @ Shoreline)
Occupancy: III
Basic Wind Speed (V): 90 mph
 | Height | Kz | qz | P | Height Difference | F
First | 9 | 0.943 | 16.62 | 18.09 | 0 | 0.00
Second | 26.5 | 1.137 | 20.05 | 20.84 | 17.5 | 91.60
Third | 41.83 | 1.231 | 21.70 | 22.17 | 15.33 | 87.19
Fourth | 56.16 | 1.296 | 22.85 | 23.09 | 14.33 | 87.43
Fifth | 70.5 | 1.348 | 23.77 | 23.83 | 14.34 | 89.97
Sixth | 84.83 | 1.393 | 24.54 | 24.45 | 14.33 | 92.11
Seventh | 99.16 | 1.431 | 25.22 | 24.99 | 14.33 | 97.42
Penthouse | 114.5 | 1.467 | 25.86 | 25.50 | 15.34 | 121.17
Roof | 135.21 | 1.510 | 26.62 | 26.11 | 20.71 | 70.30
 | Force (k) | Shear (k) | Moment (ft-k)
Ground | 0 | 179 | 0
First | 92 | 175 | 1603
Second | 87 | 177 | 2863
Third | 87 | 182 | 4123
Fourth | 90 | 190 | 5533
Fifth | 92 | 219 | 6984
Sixth | 97 | 191 | 8783
Penthouse | 121 | 70 | 12783
Roof | 70 | 0 | 8873
Wind Diagram
Wind Forces
Wind Loads
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
  Gravity
  Wind
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 16
Column Redesign
Original column design
  Steel wide-flange members
Redesign
  Reinforced concrete columns w/ steel rebar
  Columns kept as small as possible to retain the light, open feel of the current design
DESIGN CRITERIA
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
  Design Criteria
  RAM Model
  Results / Architectural Impact
  Checks
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 17
Column Redesign
RAM MODEL
DL: 80 psf
LL carefully placed with floor plan
Bar configurations:
  # of bars range from 8-16
RAM Model
Front View
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
  Design Criteria
  RAM Model
  Results / Architectural Impact
  Checks
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 18
Column Redesign
RESULTS
10”x10” in penthouse
24x24” in first floor
ARCHITECTURAL IMPACT
Columns larger than anticipated
Larger columns located in more open, spacious areas
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
  Design Criteria
  RAM Model
  Results / Architectural Impact
  Checks
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 19
Column Redesign
Checks
Column D-7, Level 3
At = 847 ft2
DL = 180 psf
LL = 80 psf
Wu = 1.2(180) + 1.6(80) = 344 psf
Pu 3rd floor = = 291.37 k
Pu above floors = 1268.25 k
Pu = 291.37 + 1268.25 = 1559.2 k
MuT = 36.12 ft-k
MuB = -22.08 ft-k
H = 13.33 ft
Fy = 60 ksi
F’c = 4 ksi
14 #10 bars
ΦPn = .8Φ[.85f’c(Ag – Ast) + fy(Ast)]
Φ(1559.2) = .8Φ[.85(4)(20(20) – 14(1.27)) + 60(14)(14)(1.27)]
1559.2 < 1893.1 => ok
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
  Design Criteria
  RAM Model
  Results / Architectural Impact
  Checks
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 20
Lateral System Redesign
Original Lateral System
  K-Braced Frame with steel wide-flange and HSS members
Redesign
  Reinforced concrete shear walls
  Existing concrete walls used
    Stair wells (blue)
    Elevator shaft / mechanical space (red)
 | Force (k) | Shear (k) | Moment (ft-k)
First | 0 | 149.1 | 0
Second | 76.6 | 145.0 | 1289
Third | 72.5 | 147.1 | 2284
Fourth | 72.5 | 151.0 | 3274
Fifth | 74.6 | 151.8 | 4389
Sixth | 76.4 | 178.6 | 5536
Seventh | 75.5 | 169.3 | 6504
Penthouse | 103.1 | 66.2 | 10207
Roof | 66.2 | 0.0 | 8036
New Wind Forces
New Wind Diagram
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
  Design Criteria
  Results
CM Breadth: Cost Analysis
Flood Analysis

## Slide 21
Lateral System Redesign
Results
  Both stairwell and elevator / mechanical space walls needed
  10” walls
Wall | Reinforcement (bars) | Spacing (inches)
2 | #7 | 16
4 | #6 | 18
6 | #2 | 18
7 | #5 | 16
8 | #3 | 18
9 | #5 | 16
10 | #3 | 18
11 | #5 | 16
12 | #3 | 18
13 | #5 | 16
14 | #3 | 18
Floor | ΣKX2 | ΣKY2 | J
1st | 336,396 | 110,153 | 446,549
2nd | 486,015 | 160,457 | 646,472
3rd-Penthouse | 585,073 | 197,580 | 782,653
J-Values
Shear Wall Design
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
  Design Criteria
  Results
CM Breadth: Cost Analysis
Flood Analysis

## Slide 22
Construction Management Breadth:
Cost Analysis
Original Steel Design: $1,411,217
Concrete Redesign: $1,285, 191
  Slab: $831,960
  Columns: $383,363
  Shear Walls: $69,868
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 23
Flood Analysis
Highest flood level of James River: 22 ft
VASCIC 9 ft above sea level
Levee Design
  Soil: sand, dense and well graded
    Aesthetically pleasing
    Resists 811 lb/sf force acting on levee
    Resists seepage
  Slurry Wall: Soil-cement bentonite
    High productivity
    Verifiable continuity and depth
    Excellent resistance to contaminated water
    Ability to easily flex with ground movements
    Greater trench stability possible
    Resistant to erosion and burrowing animals
Levee Design
Introduction
Existing Structural System
Problem Statement
Proposed Solution
Architectural Breadth: Column Layout Redesign
Slab Redesign
Loads
Column Redesign
Lateral System Redesign
CM Breadth: Cost Analysis
Flood Analysis

## Slide 24
Thank You For Your Time