## Slide 1
DEVELOPING A PROTOTYPE
Now Featuring Executive Office Suites
Presented by:
Katie Ritter
Faculty Advisor:
Dr. Ali Memari

## Slide 2
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions
STRUCTURAL OPTION
Katie
Ritter
Residence Inn by Marriott
DEVELOPING A PROTOTYPE
Original Design:
Downtown Norfolk, VA
9 Stories ~ 108’ Ht.
130,000 GSF
160 Guest Suites
$22 Million
Completed January 2009
All-suite hotel for extended-stay guests
Fully-equipped kitchens in each suite
Ground floor amenities:
  Laundry facilities for guests
  Indoor pool / spa / fitness
“A home away from home.”

## Slide 3
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Proposal & Goals
DEVELOPING A PROTOTYPE
Create a new signature brand for Marriott specifically for the business traveler, adding an office suite dimension to hotel-style living.
1
Engineer a prototype structure that is suitable for numerous locations across the U.S.
2
ARCHITECTURAL BREADTH
Design new office suite floors
  Embrace upscale design
  Provide green roof space for residents
  Maintain all existing vertical transportation routes/mechanical shafts & penetrations
LIGHTING BREADTH
Innovative conference room lighting design
STRUCTURAL DEPTH (part 1)
Check original floor design for increased loads
Re-design gravity columns
Re-design transfer girders @ 2nd Floor
STRUCTURAL DEPTH (part 2)
Develop loading criteria for prototype
Apply loads to original structure & analyze
Shear wall re-design
  Develop lateral structural solution that satisfies code requirements with new demands
  Maintain original shear wall locations
  Evaluate feasibility of the prototype structure
    Variables to consider
    Cost
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 4
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Original Structural Design
DEVELOPING A PROTOTYPE
Floor System
8” slab, typical
22’ max bay size
Most economical
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 5
A
C
B
E
D
F
N
P
G
J
K
L
M
H
Q
R
S
1
3
4
6
7
8
9
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Original Structural Design
DEVELOPING A PROTOTYPE
Lateral System
(14) cast-in-place reinforced concrete shear walls
12” thick, typical
Gravity System
cast-in-place reinforced concrete columns
14” x 30”, typical
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 6
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
…a new Executive Residence Inn
DEVELOPING A PROTOTYPE
108’
24’
South Elevation
Office
Suites
Hotel
Suites
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 7
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
DEVELOPING A PROTOTYPE
Office Level Floor Plans
11th Floor Plan
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 8
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Gravity Loads
DEVELOPING A PROTOTYPE
Revised Gravity Loads (psf) |  |  |  | 
Location | Dead (Incl. Self-Wt. of Slab) |  | Live | 
 | Original | New | Original | New
Roof | 135 | 135 | 30 | 30
11th | - | 150 | - | 50/80/100
10th | - | 195 | - | 50/80/100
Typical Floors 2nd - 9th | 125 | 125 | 40 | 40
50 PSF
80 PSF
100 PSF
11th Floor
(10” slab)
10th Floor
(10” slab)
Modular system
2’x4’ typical
Lightweight
35 psf max wet modules
8 psf pavers made from recycled rubber
Flexibility
Drought-resistant choice of plantings
Customized to
each location
10” slab
required
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 9
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Gravity Column Re-Design
DEVELOPING A PROTOTYPE
A
C
B
E
D
F
N
P
G
J
K
L
M
H
Q
R
S
1
3
4
6
7
8
9
Typical Floor - Column Layout
17’
21’
11th
10th
9th
8th
7th
6th
5th
4th
3rd
2nd
1st
19’
8 @
9’-4”
2 @
12’
Upper Office Floors - Column Layout
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 10
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Gravity Column Re-Design
DEVELOPING A PROTOTYPE
11th
10th
9th
8th
7th
6th
5th
4th
3rd
2nd
1st
19’
8 @
9’-4”
2 @
12’
Original Design
14” x 30”
(10) #9
20” x 30” (12) #10
Re-Design
14” x 20”
(6) #8
20” x 30” (12) #10
Pu,max = 854 kips
4 ksi
5 ksi
Potential Shortcomings of Re-Design:
Floor slab shear reinforcement required
  Double-U Stirrup
  Shearheads
  Cost Impact
Story Drift Impact from Lateral Loads
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 11
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Loading Criteria for Prototype
DEVELOPING A PROTOTYPE
Basic Wind Speed
(3-sec. Gust)
V ≤ 120 mph
(Norfolk: V=110 mph)
Other Assumptions:
Exposure Category B
Urban & suburban areas with closely spaced obstructions
Not located on a hill
  Topo factor, kzt = 1
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 12
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Loading Criteria for Prototype
DEVELOPING A PROTOTYPE
Short Period, Ss ≤ 50
Seismic Parameters:
Spectral Response Acceleration
Long Period, S1 ≤ 15
Other Assumptions:
Site Class D ~ Stiff Soil
Seismic Design Category D
  Ordinary reinforced concrete shear walls not permitted per ASCE7-05
  Max height for special reinforced concrete shear walls = 160’
    System overstrength factor = 2.5
  Redundancy factor = 1.3
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 13
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Structural Computer Model
DEVELOPING A PROTOTYPE
Modeling Assumptions:
Shear Walls
  Shell areas
  Maximum mesh of 24”
  Cracked sections considered; 50% of stiffness
  P-Delta effects included
Floor Diaphragms
  Rigid
  Null areas with assigned area masses
Natural Periods:
Tx = 1.077 sec.
Ty = 1.436 sec.
Tz = 0.857 sec.
ETABS
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 14
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Structural Irregularities
DEVELOPING A PROTOTYPE
(1a) Torsion
in X-Direction
(1b) Extreme Torsion
in Y-Direction
(2) Reentrant Corner
@ Upper Office Floors
Y
X
Modal Response Spectrum Analysis Required
Equivalent Lateral Force procedure used to obtain seismic loads for preliminary design
Diaphragm Considerations:
Connections to Shear Walls
Model as semi-rigid
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 15
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Relative Stiffness of Shear Walls
DEVELOPING A PROTOTYPE
Chart: Y-Direction Shear Walls
| SW-3 | SW-1 | SW-6 | SW-8 | SW-14 | SW-12 | SW-10
% Lateral Resistance | 12 | 18 | 26 | 6 | 7 | 22 | 8
Wall Length (ft) | 23 | 25 | 22 | 17 | 17 | 24 | 17
Chart: X-Direction Shear Walls
| SW-2 | SW-4 | SW-5 | SW-7 | SW-9 | SW-11 | SW-13
% Lateral Resistance | 1 | 52 | 1 | 1 | 28 | 1 | 16
Wall Length (ft) | 9 | 42 | 9 | 9 | 31 | 9 | 24
Y
X
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 16
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Controlling Lateral Loads
DEVELOPING A PROTOTYPE
Chart: Unfactored Base Shear
| X-Direction | Y-Direction
Wind | 326 | 943
Seismic | 963 | 911
Critical Loads at Base of Shear Walls |  |  |  |  | 
 | Shear Wall | Controlling Load Combination | Axial | Shear | Moment
 |  |  | Pu (kips) | Vu (kips) | Mu (ft-k)
X-Direction Loading | SW-2 | (5) | 235 | 12 | 476
 | SW-4 | (5) | 2,169 | 640 | 51,115
 | SW-5 | (5) | 175 | 13 | 509
 | SW-7 | (5) | 216 | 12 | 481
 | SW-9 | (5) | 1,468 | 343 | 23,980
 | SW-11 | (5) | 235 | 16 | 678
 | SW-13 | (5) | 722 | 191 | 11,752
Y- Direction Loading | SW-1 | (4) | 1,701 | 270 | 15,350
 | SW-3 | (4) | 532 | 182 | 10,980
 | SW-6 | (4) | 2,056 | 378 | 14,626
 | SW-8 | (4) | 689 | 89 | 4,998
 | SW-10 | (4) | 424 | 121 | 7,306
 | SW-12 | (4) | 749 | 327 | 24,021
 | SW-14 | (4) | 689 | 108 | 6,117
LC (5):
1.293D + 0.5L + 0.2S + 1.3E
LC (4):
1.2D + 1.0L + 0.5Lr + 1.6W
Y
X
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 17
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Shear Wall Re-Design
DEVELOPING A PROTOTYPE
Mu = 51,115 ft-k
Pu = 2,169 k
Vu = 640 k
SW-4
Boundary Element Design
24”
40”
(16) #10
(5) #5 ties @ 6” vertical spacing
(2) curtains #9 @ 12” EW
Shear & Flexural Reinforcing
118’
42’
12”
Chart: % Material Increase Required for SW-4
| Concrete | Reinforcement
Norfolk, VA | 0.84 | 0.48
Prototype | 0.16 | 0.52
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 18
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Preliminary Prototype Feasibility
DEVELOPING A PROTOTYPE
CONS
  Potentially significant increase in material CO$T to ‘overdesign’
  Impossible to ‘pre-engineer’ completely due to multiple assumptions that must be made upfront
PROS
  Loading criteria meets demands of large geographic area
  Design capable of having minimal impact on architecture & interiors
Summary of Assumptions for Prototype
Wind
  V ≤ 120 mph
  Closely spaced obstructions nearby
Seismic
    Site Class D
    SDC-D
    Snow
      Ground snow load = 30 psf
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 19
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
Summary & Next Steps
DEVELOPING A PROTOTYPE
ARCHITECTURAL BREADTH
Design new office suite floors
  Embrace upscale design
  Provide green roof space for residents
  Maintain all existing vertical transportation routes/mechanical shafts & penetrations
LIGHTING BREADTH
Innovative conference room lighting design
STRUCTURAL DEPTHS
Check original floor design for increased loads
Re-design gravity columns
Re-design transfer girders @ 2nd Floor
Develop loading criteria for prototype
Apply loads to original structure & analyze
Shear wall re-design
  Develop lateral structural solution that satisfies code requirements with new demands
  Maintain original shear wall locations
  Evaluate feasibility of the prototype structure
    Variables to consider
    Cost
Conference room lighting design
Re-design of transfer girders
Perform modal response spectrum analysis & identify if resulting loads are more critical than ELF
  Re-design & re-model shear walls based on updated loads
    Reinforcement detail @ openings
    Check drift & modify as necessary
    Re-check column design with displacements
    Cost analysis of prototype
NEXT STEPS…
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions

## Slide 20
Faculty Advisor:
Dr. Ali Memari
The Pennsylvania
State University
April 14, 2009
STRUCTURAL OPTION
Katie
Ritter
QUESTIONS?
DEVELOPING A PROTOTYPE
Special thanks to:
Advisor: Dr. Ali Memari
Dr. Andres Lepage
Professor Kevin Parfitt
Holbert Apple Assoc.
LTD Management Co.
JN+A
Clancy + Theys Construction Co.
AE Faculty & Staff
Family & Friends
Residence Inn
Proposal & Goals
Original Structure
Architectural Design
Gravity System Re-Design
Lateral System Re-Design
Summary & Next Steps
Questions