## Slide 1
The Optimus
Signature Boutique Offices , India
AE Senior Thesis 2013
Punit G. Das | Structural Option
Faculty Advisor: Dr. Linda Hanagan
Notes: Personal introduction

## Slide 2
The Optimus | India
Building Information
Location and Site Map
Main Street
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Office + Parking garage + Retail
Ground + 17 floors
430,000 sq. ft.
Max height: 230 ft.
January 2012 – October 2013

## Slide 3
The Optimus | India
Project Team
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Owner + Project Manager + General Contractor: Lodha Group
Architect: Pei Cobb Freed & Partners, New York
Local Architect: Edifice Consultants Pvt. Ltd.
Structural Engineer: Leslie E. Robertson Associates
MEP Consultant: Spectral Consultants Pvt. Ltd.
Lighting Designer: George Sexton Associates

## Slide 4
The Optimus | India
Building Information
Architecture
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Open Floor Plan
South facing offices for panoramic views
Balconies on every floor
Façade: Glass + Aluminum + Stone, designed for
Roof garden + Cafeteria + Gymnasium
South facing offices
Balcony

## Slide 5
Architecture
The Optimus | India
Existing Gravity System
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Open floor plan: Perimeter columns + 1 row of interior columns
8” flat slabs with additional 8” drop panels
3’x1.5’ to 3’x7’ rectangular columns for parking space
1.5’ to 3’ diameter circular columns in office spaces
Building façade supported at cantilevered slab edges
Concrete strength range from 5000 psi to 7000 psi

## Slide 6
Facades
Architecture
The Optimus | India
Existing Lateral System
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Reinforced concrete shear walls ranging from 12” to 20”
8 ft. to 25ft. walls in North-South direction and 47 ft. wall in East-West direction
Shear walls wrap the elevator shaft and stairwells
Due to proximity to the Arabian sea, wind loads control the lateral system
Shear wall layout

## Slide 7
Facades
Architecture
The Optimus | India
Concrete in India
Mumbai
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Concrete is a most prevalent building material
Mumbai is called Concrete Jungle
Client’s perception that concrete is cheap
Cheap labor
Cheap design consultation
Concrete design is comfort zone of most architects and engineers
Lack of steel construction firms
Image Courtesy of www.skyscrapercity.com

## Slide 8
Facades
Architecture
The Optimus | India
Problems with concrete
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Environmental impact
Hard to maintain quality control in India
Cheap labor can sometimes be harmful.
Member sizes get huge with taller buildings
Future challenges require alternate materials
Image Courtesy of The Hindu Newspaper
Building collapse in Mumbai
Notes: Problem:
The construction of the building follows the general trend of concrete construction that has been followed in india.
Concrete is said to be a profitable choice as it is a more prevalent material.
Labor is cheap for concrete construction, “The average salary of an on-site worker on a construction projetc is ____ INR which converts to ____USD.
Longer construction time, dust and noise becomes a nuisance in a densely constructed city like mumbai, in tight sight conditions  high rise construction results in large columns and walls sizes.
Does not provide space for future in an ever-growing city like mumbai.
Environmental impacts of using concrete.
SPACE challenge: densest city on planet earth. ¾ size of NYC.

## Slide 9
Facades
Architecture
The Optimus | India
Solution
Thesis Preview
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Explore benefits of Steel design
Requires less but skilled labor
Quality control easier
Taller building can have smaller members
Reduced weight of overall structure
Analyze and design of gravity members
Analyze and design lateral system
Typical steel-connection design
Cost-benefit analysis
Integration and optimization with architecture
Integration and optimization of facade
Notes: Solution:
Therefore, solution is steel
Environmental benefits, less reliance on scarce resources like water.
Structure uses less space
Faster construction
less disturbance to surrounding building in terms on pollution
Highrise building can be constructed faster  catch up with economic growth of china and other fst growing eastern economies
It has already embraced steel conctruction : mumbai airport, 40 story tallest steel building in india

## Slide 10
Facades
Architecture
The Optimus | India
New Gravity system
Structural floor plan
Building Information
Existing structural system
Thesis Statement
Thesis Solution
New Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Interior gravity columns - Steel wide-flange columns encased with reinforced concrete
Edge columns – W14 and W12 Steel wide flange
Superimposed dead Loads used from existing system
Critical design load combination - 1.2Dead +1.6Live+0.5Roof Live (ASCE 7-10)
Parking floor plan
Office floor plan

## Slide 11
Facades
Architecture
The Optimus | India
New Gravity system
Building Information
Existing structural system
Thesis Statement
Thesis Solution
New Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Following AISC Manual Chapter I
Columns mainly checked for compression, minimum size of steel core and critical elastic bucking
Composite columns caused 40% reduction in column size in parking spaces compared to existing system

## Slide 12
Facades
Architecture
The Optimus | India
Integration to architecture
Typical office floor plan
Building Information
Existing structural system
Thesis Statement
Thesis Solution
New Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Optimized open floor plan
Increased floor space in office and parking
Less obstruction of interior columns to daylight
Concrete encasing has fire-proofing advantage
Restrooms
Small columns can be integrated easily in the space
Elevator shafts
Office Space
Utility areas
Stairwell
Stairwell
Typical office floor plan

## Slide 13
Facades
Architecture
The Optimus | India
Composite Floor System
Building Information
Existing structural system
Thesis Statement
Thesis Solution
New Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
For typical office floor W14x30 beam and W18x46 girder with 1.5VLI20 Vulcraft deck used
Steel deck runs perpendicular to beam and parallel to girder
1.2Dead + 1.6Live load combination used
AISC Manual table 3.21 and 3.20 used to design a partially composite section
Composite system cross-section

## Slide 14
Facades
Architecture
The Optimus | India
Building Information
Lateral system
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
2 Moment frames in North-south direction
2 Braced frames in North-South direction
2 Braced frames in East-West direction
All columns are steel wide flange W12 encased in reinforced concrete. Size range – 34” to 24”
All columns designed for compression created due to lateral loads

## Slide 15
Facades
Architecture
The Optimus | India
Building Information
Lateral system
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
ASCE 7-10 Directional procedure used to calculate wind loads and drifts
ASCE 7-10 Equivalent Lateral Force Procedure and Modal Response Spectrum Analysis used
The two seismic analysis procedures compared based on drifts and base shears
Drifts (inches)

## Slide 16
Facades
Architecture
The Optimus | India
Building Information
Lateral system
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Critical seismic loads compared to critical wind load based on drifts
Design controlled by drifts and base shears due to Wind loads
Story Drifts (inches)

## Slide 17
Facades
Architecture
The Optimus | India
Integration to Architecture
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Moving braces to exterior creates more open space
Exposing HSS braces as architectural elements
Moving braces help improve parking space
Elevator shaft moved around braces to create more parking space
Elevator shaft moved
Parking Floor plan

## Slide 18
Facades
Architecture
The Optimus | India
Connection Design
Moment frame
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion

## Slide 19
Facades
Architecture
The Optimus | India
Effect on foundations
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Existing building has 50” to 80” thick MAT foundation
Dead load on foundation reduced from 25000 kip to 23000 kip

## Slide 20
Facades
Architecture
The Optimus | India
Acknowledgements
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Family and friends
Engineers at Leslie E. Robertson Associates (New York and Mumbai offices)
Pei Cobb Free & Partners Architects
Lodha Group
The AE faculty

## Slide 21
Facades
Architecture
The Optimus | India
Conclusion
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Cost benefit analysis resulted in higher price of steel structure
However, increased floor space area, faster construction and reduced labor can cover up the extra cost of steel structure
Every structural change follows architectural integration
Adding steel building to skyline of Mumbai can improve city’s image of concrete jungle
Composite columns can be of great structural and architectural advantage to tall structures

## Slide 22
Facades
Architecture
The Optimus | India
Steel structural system
Concrete structural system
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion

## Slide 23
Facades
Architecture
The Optimus | India
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Appendix

## Slide 24
Facades
Architecture
The Optimus | India
Building Information
Existing structural system
Thesis Statement
Thesis Solution
Gravity System
Composite Floor system
Lateral System
Moment Connection Design
Effect on foundations
Conclusion
Appendix
R1
R2
R3
R4