## Slide 1: Apollo
Rebecca Bires | Scott Brown | Scott Eckert | Jordan Huey | Helen Leenhouts | Andrew Levy | Jeffrey Loeb | Patrick Vogel

## Slide 2
Apollo
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
30 Story Mixed-Use High-Rise
4 Story Lobby
Restaurant
Retail
25 Office Floors
4 Story Underground Parking Garage
San Francisco , CA
350 Mission

## Slide 3
  Net-Zero Design
  Seismic Activity Response
  High Quality for Occupants
  Producing energy
  Reducing energy load
  Continuous operation after a design level earthquake
  Half of code allowed drift
  System performance
Project Goals
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 4: Net Zero
Net Off-Site Energy Use (ZEB) - 100% of the energy purchased comes from renewable energy sources, even if the energy is generated off the site.
Strategy: buy energy from renewable sources and PV Eco-districts.
Goal: 35%
Net-Zero Source Energy Use (ZNE) - The building generates the same amount of energy that it consumes.
Strategy: use a combined heat-and-power system to generate energy on-site.
Goal: 20%
Net-Zero Energy Emissions (ZEE) – A building with zero net carbon emissions.
Strategy: use algae bioreactors to offset the carbon emissions of the combined
heat-and-power system.
Goal: 50%
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Notes: *Reference Goals based off of PG&E website information and 201 Mission Street case study

## Slide 5: Building Overview
Price Estimate: $93 million
Schedule: 2.5 - 3 years
LEED Certification: Platinum
Systems
  Double Façade
  Raised Access Floor System
  Structural Steel System
  Photovoltaic Grid
  Combined Heat and Power
4 Story Parking Garage
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 6
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Mission Street
Fremont Street
  Street Level
  Lower Lobby
  Retail
  Back of House
  Elevator Lobby
  Second Level
  Upper Lobby
  Restaurant
  Elevator Lobby
  Staircase
Lobby Layout

## Slide 7
  Conference Rooms
  Partner Offices
  Executive Offices
  Reception
  Elevator Lobby
  Ancillary Spaces
  Open Offices
Typical Office Layout
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 8: Project Phasing
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 9: Demolition Phase
Electric Bus Lines
Asbestos Abatement
Demolition Mat
Sort & Recycle off-site
Concrete Reuse
Off Site Trailer
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 10: Excavation Phase
Construction Fence
Soil Conditions
Retaining Wall
Foundation Mat
$5 million
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 11: Erection Phase
Office Location
Crane Location
Safety
Electric Bus Lines
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 12: Systems
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 13: Daylight
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 14
Typical Office Layout
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
  Clear Glass Walls
  Frosted Glass Walls
  Half Height Walls

## Slide 15
Non-Dimmed
Non-Dimmed
Energy Use Reduction
Vacancy Sensing
Light Level Tuning
Daylight Harvesting
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 16
Vacancy Sensing
turning off lights in unoccupied spaces
29,000 kWhr
Light Level Tuning
continually reducing lighting output, until it is too low
24,700 kWhr
Daylight Harvesting
dimming 38 fixtures to an average level of 24%
98,300 kWhr
LPD Reduction
0.67 W/ft2 out of 0.9 allowable, 36% reduction
191,360 kWhr
Total
383,814 kWhr
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Energy Savings

## Slide 17: Double Façade ~$13 M
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 18: Double Façade
Summer Conditions (>74oF) | 
Window Layer | Action
Outer | Open
Plenum | Opens when plenum >85oF
Inner | Closed
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 19: Double Façade
Winter Conditions (0-45 oF) | 
Window Layer | Action
Outer | Closed
Plenum | Opens when plenum >85oF
Inner | Opens when plenum > 70
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 20: Double Façade
Natural Ventilation Conditions (55-74oF) | 
Window Layer | Action
Outer | Open
Plenum | Opens when plenum >85oF
Inner | Open
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 21: Raised Floor ~ $6 M
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 22: Raised Floor
  Pods
  Raised Floor System
  Walls that penetrate the raised floor
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Notes: Benefits
IAQ
Less conditioning
No short circuit
Flexibility
Why chose over radiant – immediate occupancy
Seismic Bracing
Pods – CM (location of underfloor) and Structural (weight)

## Slide 23: Raised Floor
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Notes: Benefits
Seismic Bracing

## Slide 24: Gravity Elements ~ $5.5 M
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 25: Gravity Elements
Steel Super-Structure
Design Considerations:
  Long span conditions for steel beams
  Limit excessive beam depths
  Limit Floor to Floor height increase
Loads:
  Live Load: 100 psf
  Dead load: self weight + 10 psf
  Partition Load: 20 psf
  Raised Floor: 10 psf
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 26: Gravity Elements
Strategy
  RAM SS was used to design all gravity elements
  Initial RAM model was built for a typical floor with non-composite beams and unreducible loads to determine a worst case beam depth
  Team check-in to discuss beam depths
  RAM model rebuilt to a typical floor with composite beams and reducible loads
Structural Elements
  Beams range from W14 shapes to W36 shapes
  All columns in upper floors are W14 shapes
  Built up columns were designed where W14 had inadequate capacity
  2VLI20 deck from the Vulcraft Manufacturer’s catalog was used with a 4 ½ inch topping thickness of normal weight concrete (2 hour fire rating)
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 27: Gravity Elements
Typical Floor Beam Layout
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 28: Gravity Elements
Columns
  Spliced every 2 levels
  W14 shape
  Built-up columns designed in lower levels
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 29: Gravity Elements
Problems
  Beam depths still excessive
  Cantilever
Solution
  Interior columns added, new spaces created
  Corner column introduced above lobby level, cantilever now only exists at lobby level
  Transfer braces added to cantilevered corner to transfer load away from corner
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 30: Lateral Elements ~ $15 M
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 31: Lateral Elements
Design considerations:
  Building is to be able to withstand a design level earthquake with near immediate occupancy required after the event.
  The structure is to comply with one half the code allowed drift limit.
  While economy is not explicitly mentioned in the competition guidelines, the design team did consider the cost of different systems.
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 32: Lateral Elements
Initial Strategy:
  Remove concrete structure as the primary LFRS and replace with steel
  Determine the new drift limit for the high rise
  Investigate potential damping systems
  Propose a new LFRS based on investigation and check progress for drift and ease of repair after a seismic event
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Notes: Concrete will require more effort to repair after a design level earthquake and will be harder to attain the drift limit described in the competition guidelines.
The team proposed an estimated height for the building after a redesign in steel in order to obtain the story drift allowed by the competition
With a strict drift limit such as that imposed by the competition the design team wanted to explore all options for reducing story drift.

## Slide 33: Initial Lateral Calculations
Equivalent Lateral Force
  Performed for the estimated design weight in order to determine the approximate forces that the design team would be dealing with
Revised drift limit
  Upon accounting for extra height imposed by the new steel construction and mechanical systems the drift limit was determined to be 41.5 inches at the full height of the building
Level | Fx (kips) | M (kip-ft)
Roof | 221.60 | 85130.23
26 | 207.66 | 76835.23
25 | 195.04 | 69598.54
24 | 182.76 | 62809.38
23 | 170.82 | 56455.63
22 | 159.21 | 50525.63
21 | 147.96 | 45005.28
20 | 137.05 | 39883.79
19 | 126.50 | 35147.91
18 | 116.31 | 30784.84
17 | 106.49 | 26781.59
16 | 97.03 | 23125.00
15 | 87.94 | 19801.73
14 | 79.24 | 16798.22
13 | 70.92 | 14100.72
12 | 62.99 | 11695.24
11 | 55.46 | 9567.51
10 | 48.34 | 7703.02
9 | 31.64 | 6086.94
8 | 35.37 | 4707.10
7 | 29.53 | 3538.98
6 | 24.15 | 2575.59
5 | 19.22 | 1797.51
4 | 14.78 | 1187.73
3 | 10.85 | 728.58
2 | 7.44 | 401.59
Lobby | 0.00 | 0.00
 | 2456.30 | 702769.9
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 34: Lateral System Investigation
After performing the initial calculations and discovering the significant forces on the building, lateral systems and damping were investigated. This investigation included:
Base Isolation
Outrigger systems
Damping systems (primarily viscous fluid damping)
Steel plate shear walls
Special braced and moment frames
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Notes: Base isolation was not appropriate for a building of this size
Used primarily for buildings with a period around 1s, while 350 mission will be on the range of 2-3s
Outrigger systems utilize the entire building footprint, but for a project of this scale the technique is excessive
Viscous fluid damping
Only assists with energy dissipation and reduction of drift
This means that strength is actually lost due to replacing cross members with dampers
An expensive solution to the problem
Steel plate shear walls
Potentially expensive, but adds considerable lateral strength and stiffness
Braced and moment frames
Common practice for a building this size, provides an accessible space, and adds strength and stiffness to the lateral system.

## Slide 35: New Lateral Calculations
Equivalent Lateral Force
  Performed for the proposed steel structure with estimated lateral members
Increased loads and moments at each floor
Level | Fx (kips) | M (kip-ft)
Roof | 258.12 | 114603.37
30 | 194.45 | 83419.72
29 | 182.84 | 75695.71
28 | 171.53 | 68441.00
27 | 160.53 | 61643.12
26 | 153.02 | 56465.09
25 | 142.42 | 50417.00
24 | 132.14 | 44796.41
23 | 122.19 | 39590.04
22 | 115.81 | 35785.56
21 | 106.26 | 31239.88
20 | 97.05 | 27078.25
19 | 88.21 | 23286.27
18 | 80.14 | 19955.64
17 | 71.98 | 16842.28
16 | 64.18 | 14055.75
15 | 56.77 | 11580.62
14 | 51.01 | 9640.52
13 | 44.21 | 7692.35
12 | 37.82 | 6014.15
11 | 31.87 | 4588.70
10 | 26.59 | 3429.76
9 | 21.47 | 2447.39
8 | 16.82 | 1665.09
7 | 12.66 | 1063.25
6 | 9.45 | 652.03
5 | 6.18 | 333.92
Restaurant | 0.58 | 10.52
Lobby | 0.00 | 0
 | 2456.3 | 812433.396
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 36: Final Lateral Design
Composed of special concentrically braced frames in the core
  Includes moment frames on the perimeter as required by code although the core alone meets requirements
Originally composed of SPSW and braced frames
  SPSW actually proved to be not only stiffer than was needed, but also significantly more expensive than the final design.
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 37: Final Lateral Design
Drift achieved: 39 inches
  Compare to 41.5 inch requirement
    Neither over nor under-designed
    Results in an economic design meeting requirements
Withstands normal low magnitude seismic events
Minimal drift during design level events and presents an easily repairable structure.
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 38: Photovoltaic ~$510,000
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 39: Photovoltaic System
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Size
816 Photovoltaic panels mounted on 68 telescoping poles
Distribution
Transformed and fed into a distribution panel in rooftop electrical room
Output
313,250 kBTU per year
Over 3% of total energy use

## Slide 40: Combined Heat and Power ~$815,000
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 41: Combined Heat and Power
Feasibility
    High Electric Rates: $0.18/kWh
  Desirable Spark Spread: $0.10/kWh
    Future Energy Cost Concerns: Yes
    Reducing Environmental Impact: Yes
Simple Payback Period (SPP)
  Initial System Cost $815,000 California CHP/Cogeneration Incentives Rebates $312,000
Capital Cost Post Rebate $503,000
    Annual Operational Savings $101,400
SPP = = = 5 years
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 42: Combined Heat and Power
Electrical Output
  Generation Capacity: 650 kW
  Generated Power: 1,014,000 kWh/yr
  Electrical Capacity Met: 27%
Thermal Output
  Heat Recovery: 1,850 MBtu/hr
  Heat Recovery Efficiency: 45%
  Heat Capacity Met: 88%
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 43: Combined Heat and Power
CHP Fuel Savings and Carbon Emission Reduction
Fuel Savings: 625 MCF (5%)
Carbon Reduction: 355,663 lbs. CO2 (20%)
350 Mission
CHP
74%
Electricity
Heat
System Efficiency Model
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Power Plant
Boiler
Electricity
Heat
33%

## Slide 44: Algae Bioreactors
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 45: Algae Bioreactors
Carbon Reduction
  Yearly Emissions: 1,369,638 lbs. CO2
  Algae Sequestration: 837,503 lbs. CO2
  Percent Reduction: 60%
Photosynthesis Chemical Reaction:
6CO2 + 12H2O + Light → C6H12O6 + 6O2 + 6H2O
Algae Bioreactor Cylinders
CO2 Intake (Connected to CHP flue gas exhaust)
Degassing Column
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 46: Results
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 47: Energy Savings
Baseline
Proposed
Plug Load
4,900,000 kBtu
Lighting
1,456,000 kBtu
Heating
1,870,000 kBtu
Cooling
517,000 kBtu
Pumps
38,000 kBtu
Heat Rejection
419,000 kBtu
Fans
1,240,000 kBtu
Plug Load
4,900,000 kBtu
Lighting
4,567,000 kBtu
Heating
4,625,000 kBtu
Cooling
1,550,000 kBtu
Pumps
155,000 kBtu
Heat Rejection
481,000 kBtu
Fans
6,578,000 kBtu
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo
Total
10,440,000 kBtu
Total
22,856,000 kBtu
46%
Notes: Special duct braces for vibrations (and piping)

## Slide 48: Achievements
Building Energy Use Reduction: 30% 54%
Net-Zero Energy Emissions: 50% 68%
Net-Zero Source Energy Use: 20% 30%
Net Off-Site Energy Use: 35% 19%
Drift Limit: 41.5 in 39 in
Lifecycle 5 yrs -
Schedule Time 2.5 yrs -
Goal Achieved
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 49: LEED
Project Checklist | Possible Points
Sustainable Sites | 21
Water Efficiency | 6
Energy and Atmosphere | 26
Materials and Resources | 8
Indoor Environmental Quality | 12
Innovation and Design Process | 3
Regional Priority Credits | 4
Total | 80
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo

## Slide 50
350 Mission
An iconic building that sets a precedent for sustainable architecture in San Francisco
Introduction | Phasing | Daylight | Double Façade | Raised Floor | Gravity | Lateral | Photovoltaic | CHP | Algae | Results
Apollo