## Slide 1
Penn State University
Kevin Andreone
Mechanical Option
Advisor: Dr. Laura Miller
Senior Thesis Presentation

## Slide 2
Introduction
  Building Overview
  Existing Mechanical
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions
Building Overview
General Building Data
Location:
Size:
Height:
Construction Dates:
Cost:
Occupancy
Project Team
Owner:
Architect:
MEP/FP Engineer:
Structural Engineer:
Civil Engineer:
Project Management:
Washington, DC
54,000 GSF
4 Stories above grade, 1 below
July 2013-May 2014
15 million
Administrative/Office
Catholic University of America
SmithGroupJJR
SmithGroupJJR
McMullan & Associates, Inc.
ADTEK
Mark G Anderson Consultants, Inc.
Site Analysis

## Slide 3
Existing Mechanical Systems
Air-Side
3 Existing AHU’s
  East wing not in scope
AHU-4 and AHU-6
  Use VAV and Fan powered boxes with hot water reheat in basement and first floors
AHU-5
  Displacement ventilation on first floor for two story banquet hall
OAHU-1
  Dedicated Outdoor AHU
  Ventilates floors 2-4 and uses 4 pipe Fan Coil Units
Basement Floor
1st Floor
2nd Floor
3rd Floor
4th Floor
(E)-Existing
Introduction
  Building Overview
  Existing Mechanical
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions

## Slide 4
Existing Mechanical Systems
Basement Floor
1st Floor
2nd Floor
3rd Floor
4th Floor
(E)-Existing
Water-Side
Cooling
One 97.7 ton electric air-cooled chiller
  Two chilled water pumps with VFD’s
Heating
Two 500 MBH Condensing Boilers
  84% Efficient
  Low Pressure (2psi) 2 inch gas pipe provided by Washington Gas Company
  Three hot water pumps with VFD’s
Introduction
  Building Overview
  Existing Mechanical
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions

## Slide 5
CHP Introduction
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Introduction
CHP Goals
Simultaneous production of heat and power with on-site generation
Reliable power during grid blackout or brownout
Higher overall efficiencies
Lower emissions
Absorption Cooling Goals
Utilize waste heat in summer months
Reduce existing chiller size
Reduce power demand in summer months

## Slide 6
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Spark Gap
Difference between price of natural gas and electricity
Building Demand Profiles
Demands
Thermal to power ratio
λD = Qq
Qe
Driving factor
Chart: 24 Hour Building Demands per Month

## Slide 7
Microturbine
Produce lowest power(15-250KW)
Low electrical Efficiency
Low Maintenance Cost
Low emissions
Table from EPA
Capstone C30 Microturbine
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Prime Movers

## Slide 8
Microturbine
Produce lowest power(15-250KW)
Low electrical Efficiency
Low Maintenance Cost
Low emissions
Capstone C30 Microturbine
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Prime Movers

## Slide 9
Microturbine
Produce lowest power(15-250KW)
Low electrical Efficiency
Low Maintenance Cost
Low emissions
Capstone C30 Microturbine
Net Heat Rate
Chart: Fuel Input and Useful Exhaust vs KW Produced
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Useful Exhaust | 0 | 7860 | 15720 | 23580 | 31440 | 39300 | 47160 | 55020 | 62880 | 70740 | 78600 | 86460 | 94320 | 102180 | 110040 | 117900 | 125760 | 133620 | 141480 | 149340 | 157200 | 165060 | 172920 | 180780 | 188640 | 196500 | 204360 | 212220 | 220080 | 227940 | 235800
Fuel Input | 0 | 13100 | 26200 | 39300 | 52400 | 65500 | 78600 | 91700 | 104800 | 117900 | 131000 | 144100 | 157200 | 170300 | 183400 | 196500 | 209600 | 222700 | 235800 | 248900 | 262000 | 275100 | 288200 | 301300 | 314400 | 327500 | 340600 | 353700 | 366800 | 379900 | 393000
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions

## Slide 10
Microturbine
Produce lowest power(15-250KW)
Low electrical Efficiency
Low Maintenance Cost
Low emissions
Capstone C30 Microturbine
Net Heat Rate
Chart: Load Duration Curve
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions

## Slide 11
Chart: 24 Hour Heating Demands
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
January Sample Calculations
Heating Demands

## Slide 12
Chart: 24 Hour Cooling Demands
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
January Sample Calculations
Cooling Demands

## Slide 13
Chart: 24 Hour Power Distribution
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
January Sample Calculations
Power Demands

## Slide 14
Chart: 24 Hour Waste Heat Usage
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
January Sample Calculations
Useful Waste Heat

## Slide 15
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
PEUF SHP= hGTDhB(1 + l D)
hB + hGTDl D
PEUF CHP= heCHP( 1 + l D)
PEUF Hybrid = hCHPhGTDhB (1 + lD )
(hCHPhBfeD,GTD + hGTDhBfeD,CHP + hGTDhCHP l QD, B
CHP vs SHP
CHP INPUT |  | 
ήCHP | 0.26 | 
KW Produced | 30 | kw
Net Heat Rate | 13100 | btu/kw
ήHRU | 0.6 | 
ήB | 0.84 | 
ήGTD | 0.33 | 
Absorption Chiller COP | 0.7 | 
Primary Fuel Utilization Efficiency
Chart: Primary Fuel Utilization Efficiency
| 0 | 0.1 | 0.2 | 0.30000000000000021 | 0.4 | 0.5 | 0.60000000000000042 | 0.7000000000000004 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2000000000000002 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7000000000000002 | 1.8 | 1.9000000000000001 | 2 | 2.1 | 2.2000000000000002 | 2.3000000000000003 | 2.4000000000000004 | 2.5 | 2.6 | 2.7 | 2.8000000000000003 | 2.9000000000000004 | 3 | 3.1 | 3.2 | 3.3000000000000003 | 3.4000000000000004 | 3.5 | 3.6 | 3.7 | 3.8000000000000003 | 3.9000000000000004 | 4 | 4.1000000000000005 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.6000000000000005 | 4.7 | 4.8000000000000007 | 4.9000000000000004 | 5
SHP | 0.33 | 0.34928 | 0.36715 | 0.38377 | 0.39926 | 0.41373 | 0.42728 | 0.44 | 0.45196 | 0.46322 | 0.47385 | 0.48389 | 0.4934 | 0.50241 | 0.51097 | 0.5191 | 0.52684 | 0.53422 | 0.54126 | 0.54798 | 0.5544 | 0.56055 | 0.56644 | 0.57208 | 0.5775 | 0.5827 | 0.5877 | 0.59251 | 0.59714 | 0.6016 | 0.6059 | 0.61005 | 0.61405 | 0.61792 | 0.62165 | 0.62526 | 0.62876 | 0.63214 | 0.63542 | 0.63859 | 0.64167 | 0.64465 | 0.64755 | 0.65036 | 0.65309 | 0.65574 | 0.65832 | 0.66083 | 0.66327 | 0.66564 | 0.66795
Hybrid | 0.26 | 0.286 | 0.312 | 0.338 | 0.364 | 0.39 | 0.416 | 0.442 | 0.468 | 0.494 | 0.52 | 0.546 | 0.572 | 0.598 | 0.624 | 0.65 | 0.676 | 0.702 | 0.728 | 0.754 | 0.78 | 0.806 | 0.832 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858
PFESR | -0.26923 | -0.22125 | -0.17677 | -0.13541 | -0.096866 | -0.06085 | -0.027123 | 0.0045249 | 0.034281 | 0.06231 | 0.088757 | 0.11375 | 0.13742 | 0.15985 | 0.18114 | 0.20138 | 0.22065 | 0.23901 | 0.25652 | 0.27324 | 0.28923 | 0.30453 | 0.31919 | 0.33324 | 0.32692 | 0.32086 | 0.31503 | 0.30943 | 0.30403 | 0.29883 | 0.29382 | 0.28899 | 0.28432 | 0.27982 | 0.27546 | 0.27126 | 0.26718 | 0.26324 | 0.25942 | 0.25572 | 0.25214 | 0.24866 | 0.24528 | 0.24201 | 0.23882 | 0.23573 | 0.23273 | 0.2298 | 0.22696 | 0.22419 | 0.2215
FED,CHP | 0 | 0.058559 | 0.11712 | 0.17568 | 0.23423 | 0.29279 | 0.35135 | 0.40991 | 0.46847 | 0.52703 | 0.58559 | 0.64414 | 0.7027 | 0.76126 | 0.81982 | 0.87838 | 0.93694 | 0.9955 | 1.0541 | 1.1126 | 1.1712 | 1.2297 | 1.2883 | 1.3468 | 1.4054 | 1.464 | 1.5225 | 1.5811 | 1.6396 | 1.6982 | 1.7568 | 1.8153 | 1.8739 | 1.9324 | 1.991 | 2.0495 | 2.1081 | 2.1667 | 2.2252 | 2.2838 | 2.3423 | 2.4009 | 2.4595 | 2.518 | 2.5766 | 2.6351 | 2.6937 | 2.7523 | 2.8108 | 2.8694 | 2.9279
Fed,GTD | 1 | 0.94144 | 0.88288 | 0.82432 | 0.76577 | 0.70721 | 0.64865 | 0.59009 | 0.53153 | 0.47297 | 0.41441 | 0.35586 | 0.2973 | 0.23874 | 0.18018 | 0.12162 | 0.063063 | 0.0045045 | -0.054054 | -0.11261 | -0.17117 | -0.22973 | -0.28829 | -0.34685 | -0.40541 | -0.46396 | -0.52252 | -0.58108 | -0.63964 | -0.6982 | -0.75676 | -0.81532 | -0.87387 | -0.93243 | -0.99099 | -1.0495 | -1.1081 | -1.1667 | -1.2252 | -1.2838 | -1.3423 | -1.4009 | -1.4595 | -1.518 | -1.5766 | -1.6351 | -1.6937 | -1.7523 | -1.8108 | -1.8694 | -1.9279

## Slide 16
Primary Fuel Utilization Efficiency (PUEF)
λD < 0.7 SHP has a higher PUEF
λD > 0.7 CHP has a higher PUEF
λD > 1.7 start over producing electricity and start to lose money
λD = 2.3 maximum PUEF and percent fuel savings ratio
λD < 2.3 start supplemental boiler and PFESR starts to decline but still positive
CHP INPUT |  | 
ήCHP | 0.26 | 
KW Produced | 30 | kw
Net Heat Rate | 13100 | btu/kw
ήHRU | 0.6 | 
ήB | 0.84 | 
ήGTD | 0.33 | 
Absorption Chiller COP | 0.7 | 
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Primary Fuel Utilization Efficiency
Chart: Primary Fuel Utilization Efficiency
| 0 | 0.1 | 0.2 | 0.30000000000000021 | 0.4 | 0.5 | 0.60000000000000042 | 0.7000000000000004 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2000000000000002 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7000000000000002 | 1.8 | 1.9000000000000001 | 2 | 2.1 | 2.2000000000000002 | 2.3000000000000003 | 2.4000000000000004 | 2.5 | 2.6 | 2.7 | 2.8000000000000003 | 2.9000000000000004 | 3 | 3.1 | 3.2 | 3.3000000000000003 | 3.4000000000000004 | 3.5 | 3.6 | 3.7 | 3.8000000000000003 | 3.9000000000000004 | 4 | 4.1000000000000005 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.6000000000000005 | 4.7 | 4.8000000000000007 | 4.9000000000000004 | 5
SHP | 0.33 | 0.34928 | 0.36715 | 0.38377 | 0.39926 | 0.41373 | 0.42728 | 0.44 | 0.45196 | 0.46322 | 0.47385 | 0.48389 | 0.4934 | 0.50241 | 0.51097 | 0.5191 | 0.52684 | 0.53422 | 0.54126 | 0.54798 | 0.5544 | 0.56055 | 0.56644 | 0.57208 | 0.5775 | 0.5827 | 0.5877 | 0.59251 | 0.59714 | 0.6016 | 0.6059 | 0.61005 | 0.61405 | 0.61792 | 0.62165 | 0.62526 | 0.62876 | 0.63214 | 0.63542 | 0.63859 | 0.64167 | 0.64465 | 0.64755 | 0.65036 | 0.65309 | 0.65574 | 0.65832 | 0.66083 | 0.66327 | 0.66564 | 0.66795
Hybrid | 0.26 | 0.286 | 0.312 | 0.338 | 0.364 | 0.39 | 0.416 | 0.442 | 0.468 | 0.494 | 0.52 | 0.546 | 0.572 | 0.598 | 0.624 | 0.65 | 0.676 | 0.702 | 0.728 | 0.754 | 0.78 | 0.806 | 0.832 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858 | 0.858
PFESR | -0.26923 | -0.22125 | -0.17677 | -0.13541 | -0.096866 | -0.06085 | -0.027123 | 0.0045249 | 0.034281 | 0.06231 | 0.088757 | 0.11375 | 0.13742 | 0.15985 | 0.18114 | 0.20138 | 0.22065 | 0.23901 | 0.25652 | 0.27324 | 0.28923 | 0.30453 | 0.31919 | 0.33324 | 0.32692 | 0.32086 | 0.31503 | 0.30943 | 0.30403 | 0.29883 | 0.29382 | 0.28899 | 0.28432 | 0.27982 | 0.27546 | 0.27126 | 0.26718 | 0.26324 | 0.25942 | 0.25572 | 0.25214 | 0.24866 | 0.24528 | 0.24201 | 0.23882 | 0.23573 | 0.23273 | 0.2298 | 0.22696 | 0.22419 | 0.2215
FED,CHP | 0 | 0.058559 | 0.11712 | 0.17568 | 0.23423 | 0.29279 | 0.35135 | 0.40991 | 0.46847 | 0.52703 | 0.58559 | 0.64414 | 0.7027 | 0.76126 | 0.81982 | 0.87838 | 0.93694 | 0.9955 | 1.0541 | 1.1126 | 1.1712 | 1.2297 | 1.2883 | 1.3468 | 1.4054 | 1.464 | 1.5225 | 1.5811 | 1.6396 | 1.6982 | 1.7568 | 1.8153 | 1.8739 | 1.9324 | 1.991 | 2.0495 | 2.1081 | 2.1667 | 2.2252 | 2.2838 | 2.3423 | 2.4009 | 2.4595 | 2.518 | 2.5766 | 2.6351 | 2.6937 | 2.7523 | 2.8108 | 2.8694 | 2.9279
Fed,GTD | 1 | 0.94144 | 0.88288 | 0.82432 | 0.76577 | 0.70721 | 0.64865 | 0.59009 | 0.53153 | 0.47297 | 0.41441 | 0.35586 | 0.2973 | 0.23874 | 0.18018 | 0.12162 | 0.063063 | 0.0045045 | -0.054054 | -0.11261 | -0.17117 | -0.22973 | -0.28829 | -0.34685 | -0.40541 | -0.46396 | -0.52252 | -0.58108 | -0.63964 | -0.6982 | -0.75676 | -0.81532 | -0.87387 | -0.93243 | -0.99099 | -1.0495 | -1.1081 | -1.1667 | -1.2252 | -1.2838 | -1.3423 | -1.4009 | -1.4595 | -1.518 | -1.5766 | -1.6351 | -1.6937 | -1.7523 | -1.8108 | -1.8694 | -1.9279

## Slide 17
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Primary Fuel Utilization Efficiency
Chart: Hourly λD CHP
Primary Fuel Utilization Efficiency (PUEF)
λD < 0.7 SHP has a higher PUEF
λD > 0.7 CHP has a higher PUEF
λD > 1.7 start over producing electricity and start to lose money
λD = 2.3 maximum PUEF and percent fuel savings ratio
λD < 2.3 start supplemental boiler and PFESR starts to decline but still positive
CHP INPUT |  | 
ήCHP | 0.26 | 
KW Produced | 30 | kw
Net Heat Rate | 13100 | btu/kw
ήHRU | 0.6 | 
ήB | 0.84 | 
ήGTD | 0.33 | 
Absorption Chiller COP | 0.7 | 

## Slide 18
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Chart: Cost Analysis
| 0 | 1:00 AM - 10:00 PM | 2:00 AM - 9:00 PM | 3:00 AM - 8:00 PM | 4:00 AM - 7:00 PM | 5:00 AM - 6:00 PM | 6:00 AM - 6:00 PM | 7:00 AM - 6:00 PM | 8:00 AM - 6:00 PM | 9:00 AM - 6:00 PM | 10:00 AM - 6:00 PM | 11:00 AM - 6:00 PM | Noon - 6:00 PM | 24 Hours
15 KW | 0 | 18.7785 | 1087.7804 | 2013.3092 | 2782.4608 | 3498.9977 | 3961.6875 | 4420.0228 | 4801.2484 | 4674.019 | 4402.1668 | 4343.8163 | 4186.6268 | -1975.5527
30 KW | 0 | -2960.4633 | 1590.4371 | 2674.2099 | 3693.0513 | 4651.2163 | 5577.7122 | 6483.2294 | 7304.9029 | 6842.1632 | 6150.0478 | 5871.9819 | 5331.0301 | -6729.4991
65 KW | 0 | -15022.8303 | -10671.514 | -6489.6559 | -2575.1536 | 1228.7181 | 3278.6088 | 5304.6597 | 7242.1996 | 6387.9238 | 5587.0284 | 5299.8758 | 4797.2405 | -22453.3212
Cost Analysis
Cost Analysis

## Slide 19
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Chart: Cost Analysis
| 0 | 1:00 AM - 10:00 PM | 2:00 AM - 9:00 PM | 3:00 AM - 8:00 PM | 4:00 AM - 7:00 PM | 5:00 AM - 6:00 PM | 6:00 AM - 6:00 PM | 7:00 AM - 6:00 PM | 8:00 AM - 6:00 PM | 9:00 AM - 6:00 PM | 10:00 AM - 6:00 PM | 11:00 AM - 6:00 PM | Noon - 6:00 PM | 24 Hours
15 KW | 0 | 18.7785 | 1087.7804 | 2013.3092 | 2782.4608 | 3498.9977 | 3961.6875 | 4420.0228 | 4801.2484 | 4674.019 | 4402.1668 | 4343.8163 | 4186.6268 | -1975.5527
30 KW | 0 | -2960.4633 | 1590.4371 | 2674.2099 | 3693.0513 | 4651.2163 | 5577.7122 | 6483.2294 | 7304.9029 | 6842.1632 | 6150.0478 | 5871.9819 | 5331.0301 | -6729.4991
65 KW | 0 | -15022.8303 | -10671.514 | -6489.6559 | -2575.1536 | 1228.7181 | 3278.6088 | 5304.6597 | 7242.1996 | 6387.9238 | 5587.0284 | 5299.8758 | 4797.2405 | -22453.3212
Cost Analysis
Payback Period

## Slide 20
Introduction
Combined Heat and Power Analysis
  CHP Introduction
  Building Demands Profiles
  CHP Demands
  Primary Fuel Utilization Efficiency
  Cost Analysis
  Emissions
Electrical Breath
Conclusion
Acknowledgments
Questions
Emissions Spreadsheet from EPA
Emissions
Emissions

## Slide 21
Introduction
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions
Electrical Breadth
Emergency Power
150 KW emergency generator
Duel fuel microturbine to replace emergency generator
Reduce payback period
Power Connection
Replace Switchgear with Parallel Switchgear
  208/120V, 3PH-4W 3000A
  Syncs power from two sources
Add 480V:208/120V transformer
Size wires and breakers

## Slide 22
Introduction
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions
Recommendations
Recommendations
Economically
  Do not recommend CHP System
  14 year payback period
  Not enough heat load
Environmentally
  Recommend CHP system
  Save 27% Fuel Consumption
  Reduce Carbon footprint by 47%

## Slide 23
Introduction
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions
Acknowledgments
Thank You!
Dr. Laura Miller – AE Senior Thesis Advisor
SmithGroupJJR
Dr. James Freihaut – Help with CHP systems
AE Faculty and Students
Friends and Family

## Slide 24
Introduction
Combined Heat and Power Analysis
Electrical Breath
Recommendations
Acknowledgments
Questions
Questions
Questions?

## Slide 25
Questions
Cost Analysis