IE450                                                                                                Spring 2006

Homework			              	                               Dr. R. A. Wysk

Due: April 11, 2006

Prepare a Gantt chart of parts flow for the 2 CNC machine and 1 robot system shown below (as was discussed as part of the robot slides) (prepared before class on November 17)

- Two parts are made where each part goes from machine 1 – machine 2

- For part #1 processing times are: 2 and 4 minutes.

- For part #2 processing times are: 3 and 2.5 minutes

- The robot handling time is 0.25 minutes for all parts and moves

- What is the cycle time for the parts if they are batched first as 100 part #1 and then 100 part #2?

- What is the cycle time for the parts if they are run alternately part #1 and then  part #2 with this sequence repeated?

# Text boxes

UL

L

R

M2

M1

1

7

6

5

4

3

2

8