## Slide 1: 151 First Side Pittsburgh, PA
William J. Buchko
Structural Option
Senior Thesis
April 14th, 2008
Advisor: Kevin Parfitt
introduction

## Slide 2: Presentation Outline
Overview
Proposal
Structural Depth
Acoustics Breadth
Construction Management Breadth
Conclusions
Acknowledgements
Questions
introduction

## Slide 3: Overview
Location:
  Pittsburgh, PA
Significance:
  First condominium built downtown since 1968
Architecture:
  18 stories
  82 units
  Open floor plan
  233,000 SF
overview

## Slide 4: Overview
Mechanical:
  36.7 Ton roof top unit by AAON
  Individual heat pumps
Electrical:
  120/208 3 phase system
  1800a main switch
Lighting:
  Incandescent downlights in units
  Fluorescent downlights and wall washers in corridors and public areas
overview

## Slide 5: Overview
Construction:
  $24M construction cost
  Owned by Zambrano Corp., Ralph A. Falbo, Inc., and EQA Landmark Communities
  Design-build construction
Structural:
  Hambro composite joist floor system
  Braced frame and moment connection lateral system
overview

## Slide 6: Proposal
Structural Depth
  Decrease cost and increase performance by using typical structural systems
Acoustics Breadth
  Analyze proposed systems and check existing systems for acoustical quality
Construction Management Breadth
  Analyze and compare proposed systems to current systems
proposal

## Slide 7: Structural Depth
Floor System
  Current Hambro MD2000 composite joist system compared to a typical composite beam system
Lateral System
  Current combination braced frame and moment connection system compared to concrete core, braced frame, and moment connection systems
structural depth

## Slide 8: Structural Depth
Current Hambro floor system
  3¼” concrete on metal decking
  Supported by joist with composite top chord
structural depth

## Slide 9: Structural Depth
Proposed composite steel system
  4” light weight concrete on B-LOK decking with 1 stud/ft
  Beams placed at third points of bays
structural depth

## Slide 10: Structural Depth
Typical floor beam layout and design
structural depth

## Slide 11: Structural Depth
Column redesign
structural depth

## Slide 12: Structural Depth
Current lateral system
  Combination of braced frames and moment connections
structural depth

## Slide 13: Structural Depth
Frames long grids 2, 3, and 4 in north-south direction
structural depth

## Slide 14: Structural Depth
Frames long grids E and F in east-west direction
structural depth

## Slide 15: Structural Depth
Concrete core lateral system
  Utilizes concrete core to handle all lateral loading
  Unacceptable due to interaction of trades
structural depth

## Slide 16: Structural Depth
Braced frame lateral system
  Utilizes braced frames for all lateral loading
  Quicker installation
  Low torsion due to design
  Unacceptable due to diagonal braces within floor plan
structural depth

## Slide 17: Structural Depth
E
F
G
2
4
Proposed braced frame layout
structural depth

## Slide 18: Structural Depth
Moment connection lateral system
  Utilizes moment connections for all lateral loading
  Fully restrained connections recommended for greater than 10 stories
  Unacceptable due to cost and scheduling of fully restrained connections
structural depth

## Slide 19: Acoustics Breadth
Floor system
  Compare current Hambro system to proposed composite beam system
Mechanical system
  Analyze current issues and provide alternative solutions
acoustics breadth

## Slide 20: Acoustics Breadth
Current Hambro floor system
  STC of 57
  IIC of 30
  Susceptible to structure born sound
  Susceptible to “wave” phenomenon
acoustics breadth

## Slide 21: Acoustics Breadth
Proposed beam floor system
  STC of 55
  IIC of 35
  Potential for better low end absorption
  Not susceptible to “wave” phenomenon
acoustics breadth

## Slide 22: Acoustics Breadth
Mechanical system
  Roof top unit in direct line of sight with penthouse terraces
  Most common complaint from workers and potential tenants
acoustics breadth

## Slide 23: Acoustics Breadth
Existing sound levels
  AAON representative unable or unwilling to provide acoustical data
  Data obtained through IVIE IE-33 Pocket PC and similar unit
  Values were confirmed by 3rd party acoustician
acoustics breadth

## Slide 24: Acoustics Breadth
IVIE IE-33 Graph
acoustics breadth

## Slide 25: Acoustics Breadth
Proposed solutions
  Acoustical barrier would only provide 6dB reduction
  System can be relocated to minimize sound levels on terraces
acoustics breadth

## Slide 26: Acoustics Breadth
Proposed roof top unit relocation
acoustics breadth

## Slide 27: Acoustics Breadth
Relocation effects
  30ft gives 15dB reduction
  Nosier supply intake now faces away from all occupied spaces
  Two walls separate unit from terraces, adding approximately 20dB of reduction
acoustics breadth

## Slide 28: Construction Management Breadth
Schedule
  Compare scheduling impacts of proposed systems both on and off of the critical path
Cost
  Compare cost of proposed systems to current systems
cm breadth

## Slide 29: Construction Management Breadth
Schedule
  Steel placement takes 177 days and is unaffected by floor system change
  Pouring of proposed floor system would save a minimum of 1 day per floor, though not on the critical path
  A potential 10 days could be saved through fire protection
  The braced frame lateral system could save 5 days along critical path, but was found to be unacceptable
cm breadth

## Slide 30: Construction Management Breadth
Cost
  Larger slab and more expensive concrete offset with cheaper steel, resulting in a similar cost between floor systems
  Redesign of columns and beams save 131 Tons of steel, which saves approximately $228,000
  Labor savings estimated at approximately $30,000
  Total system savings over 1% of total building cost
cm breadth

## Slide 31: Conclusions
Structural Depth
  A composite beam floor system would be both feasible and economical to use
  No better lateral system was found
Acoustics Breadth
  A composite beam floor system could provide equal acoustical qualities
  Mechanical system can be moved to provide a better sound level on outdoor terraces
Construction Management Breadth
  All proposed systems could be implemented without a change in the critical path
  All proposed systems would be similar in cost or less expensive
conclusions

## Slide 32: Acknowledgements
I would like to thank the following companies and individuals:
Zambrano Corp.
The Kachele Group
Indovina Associates Architects
Hambro Systems
Cenkner Engineering Associates, Inc.
Professor Kevin Parfitt
Professor Moses Ling
The Thesis Mentors
Family and friends for their support and understanding
conclusions

## Slide 33: Dedication
This Thesis presentation and year long project is dedicated to the memory of:
Nicholas Buchko
9/15/15 – 12/6/06
“Never give up.”
conclusions

## Slide 34: Questions?
conclusions