## Slide 1
Fraser Centre
State College, PA
Tyler Strange
Structural Option
Consultant: Dr. Thomas Boothby
April 13, 2011
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 2
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011
Fraser Centre
State College, PA

## Slide 3
Introduction to Fraser Centre
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
General Information
Location……………………...State College, PA
Fraser Street and Beaver Ave
Size…………………………..230,000 sf
Project Cost…………………Unreleased
Project Team
- Architect…….……………..Wallace Roberts & Todd, LLC
- General Contractor………Leonard S. Fiore, Inc.
- Structural Engineer………David Chou & Associates, Inc.
11 story mixed-use building
  First story is parking
  Second story is parking and retail
  Third story is a theatre
  Fourth story is MEP
  Fifth-tenth stories are residential
  Eleventh story is suites
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 4
Existing System
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Floor System
Two-way 12 inch flat slab
Columns
Columns vary in size from 16in x 32in to 16in x 72in
Spans range from 28.5ft to 40ft
Shear Walls
4 shear walls located on the residential floors
Shear walls on the lower floors vary from 4 to 10
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 5
Proposal
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Depth Proposal
Change the floor system to composite concrete and steel beams for the residential levels
Redesign the residential shear walls with a new layout
Breadth Proposal
Analyze the change in cost and schedule of the new floor system
Analyze the impact the new shear wall layout will have on the architecture
Current Shear Wall Layout
Proposed Shear Wall Layout
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 6
Composite Floor
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Steel Deck: 3VLI Deck 18 Gage
B1: W12x16
B2: W10x12
G1: W18x76
G2: W16x31
C1: Welded/Bolted Single Angle L4x3x3/8
C2: Bolted/Bolted Double Angle L4x3x3/8
Load Combinations
1.2 Dead +1.6 Live
1.4 Dead
Codes:
Original design code used ASCE 7-05
New design code used ASCE 7-10
Material Strengths:
Concrete: 4000 psi
Steel: 50000 psi
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 7
Composite Floor
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Steel Deck: 3VLI Deck 18 Gage
B1: W12x16
B2: W10x12
G1: W18x76
G2: W16x31
C1: Welded/Bolted Single Angle L4x3x3/8
C2: Bolted/Bolted Double Angle L4x3x3/8
Deflection Check:
Limited to L/360
Results:
3 in 18 gage VLI steel deck was used
4.5 in of concrete was used to achieve 2 hr fire rating
W Shapes range from W10x12 to W18x76
Thickness of residential floor system was increased by 12in
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 8
Steel Connections
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Steel Deck: 3VLI Deck 18 Gage
B1: W12x16
B2: W10x12
G1: W18x76
G2: W16x31
C1: Welded/Bolted Single Angle L4x3x3/8
C2: Bolted/Bolted Double Angle L4x3x1/4
Design:
AISC Table 10-11
Girder to Beam is welded/bolted for constructability
Shear Wall to Girder is bolted/bolted for economics
Results:
Girder/Beam connection:
  Welded/Bolted Single Angle
  L4x3x3/8
  3/16th weld
  Two A325N ¾” dia. bolts
Shear Wall/Girder connection:
  Bolted/Bolted Double Angle
  L4x3x1/4
  Three A325N ¾” dia. bolts
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 9
Schedule and Cost Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Schedule Analysis
Current system takes 24 days to complete a single floor with slight overlap.
Alternative system takes 10 days to complete a single floor with a linear progression.
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 10
Schedule and Cost Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Cost Analysis
Cost of Current System
Cost of Alternative System
Description | Cost Estimate | 
In Place Forms | 2,212,344 | 
In Place Reinforcing | 3,432 | 
4 ksi Ready Mix | 60,492 | 
Placing Concrete | 37,658 | 
 | 2,313,926 | Total
Description | Cost Estimate | 
Struct. Steel W16x31 | 260,361 | 
Struct. Steel W18x76 | 829,142 | 
Struct. Steel W10x12 | 74,389 | 
Struct. Steel W12x16 | 333,575 | 
Metal Decking | 5,450,667 | 
Weld Shear Conn | 66,410 | 
4 ksi Ready Mix | 20,235 | 
Placing Concrete | 12,597 | 
 | 7,047,374 | Total
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 11
Lateral System Redesign
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Initial Shear Wall Layout
Discontinuous between parking levels, theater level, and residential levels
Architectural restraints on position and size
Proposed Shear Wall Layout
Continuous from theater level to residential levels
Number of shear walls is increased from four to seven
Shear walls are reduced in size
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 12
Lateral System Redesign
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Shear Wall Design Calculations
Flexural Reinforcement Design
Shear Reinforcement Design
  Capacity Check
  ACI Chapter 11
  Minimum Reinforcements Governed
  Spacing Limitations
3D ETABS Model
Shear walls modeled in ETABS
ETABS used to design shear walls and then checked to design by hand
Controlling Load Case:
  1.54D+1.65E
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 13
Architectural Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
5th Floor-10th Floor
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 14
Architectural Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
5th Floor-10th Floor
Largest impact on architecture occurs in Unit 3C
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 15
Architectural Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
11th Floor
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 16
Architectural Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
11th Floor
Living room width is reduced by 14”
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 17
Architectural Analysis
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
11th Floor
Bedroom width is reduced by 14”
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011

## Slide 18
Conclusion
Presentation Outline
Introduction
Existing System
Proposal
Gravity System Redesign
  Composite Floor
  Steel Connections
Schedule and Cost Analysis
Lateral System Redesign
Architectural Analysis
Conclusion
Building Weight:
  Existing System: 72,000 kips
  Proposed System: 65,000 kips
  7,000 kip reduction
Architectural Impact:
  Largest impact on floors 5-10 is shortening a single room by roughly 14”.
  Largest impact on the 11th floor is shortening the living room by 14 “.
Cost:
  Existing System: $2.3 million/residential floor
  Proposed System: $7.0 million/residential floor
  Three times more expensive
Schedule:
  Existing System: 24 days/residential floor
  Proposed System: 10 days/residential floor
  Gain 98 work days for all seven residential floors
Tyler Strange
Structural Option
Fraser Centre
Dr. Thomas Boothby
April 13th, 2011