## Slide 1: Kingstowne Section 36A Office Building with Parking Garage
PSU AE Senior Thesis
April 8, 2013
Image Provided By DCS Design
Image Provided By DCS Design
Fairfax County, VA
James Chavanic
Structural

## Slide 2: PRESENTATION OUTLINE
Image Provided By DCS Design
Image Provided By DCS Design
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS

## Slide 3: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
PROJECT INFORMATION
BUILDING OVERVIEW
200,000 SF
8 Stories (4 Parking, 4 Office)
Height = 101’-2” (86’-11” from Avg. Grade)
$ 19 Million
Construction: February 2012 – May 2013
PROJECT TEAM
Owner: Halle Companies
Architect: Davis, Carter, Scott Ltd. (DCS Design)
GC: L.F. Jennings Inc.
Civil Eng.: Tri-Tek Engineering
Mech. Eng.: Jordan & Skala Engineers
Struct. Eng.: Cagley & Associates
Image From Bing Maps

## Slide 4: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
SITE RELATIONSHIP
27’ Difference
N
Original Images: DCS Design

## Slide 5: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
EXISTING STRUCTURE
ROOF
3.25” LW Concrete on 2” 18 GA Composite Deck (Mech. Areas)
3” x 20 GA Type N Roof Deck (Remaining Areas)
Spans
  A-C 45’-0” , C-D 36’-6” , D-F 43’-6”
  East West Direction 28’-6”
Composite action in mechanical areas
(4) 17,000 lb. Roof-top Mechanical Units
Original Image: Cagley & Associates

## Slide 6: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
EXISTING STRUCTURE
OFFICE LEVELS 2 THROUGH 4
2” x 18 GA Composite Deck
3.25” LW Concrete Topping (3000 psi)
Spans
  A-C 45’-0” , C-D 36’-6” , D-F 43’-6”
  East West Direction 28’-6”
Composite action beams and girders
13’-4” Floor to floor height
Lateral System
  Moment Frames
  Concentrically Braced Frames
  Eccentrically Braced Frames
Original Image: Cagley & Associates

## Slide 7: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
EXISTING STRUCTURE
PARKING LEVELS AND OL1
8” Thick concrete flat slab
  #4 @ 12” O.C. Bottom Mat
f’c = 5000 psi
Typical bay is 28’-6” x 29’-0”
24” x 24” Typical columns
10-8” Floor to floor height
Lateral System
  12 Shear walls
  12” Thick
  f’c = 5000 psi
  #5 @ 12” O.C. Typical E.F.
Original Image: Cagley & Associates

## Slide 8: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
EXISTING STRUCTURE
FOUNDATION
All Concrete f’c = 3000 psi
48” Thick concrete mat foundations
Spread Footings
  7000 psi bearing capacity
  8’ x 8’ to 16’ x 24’
Strip Footings
  2500 psi bearing capacity
Geopiers (Rammed Aggregate Piers)
  30” Dia. 16’ deep
  100 k capacity each
Original Image: Cagley & Associates

## Slide 9: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
PROPOSED WORK
SETTING THE STAGE
Currently, no tenant selected
Police / Emergency services for Fairfax County, VA
Risk Category IV (Originally Category II)
U.S. Department of Defense Standards
www.defense.gov
www.gsa.gov
www.asce.org

## Slide 10: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
PROPOSED WORK
BREADTH 1: SITE REDESIGN
Assess potential security issues
Goal
  Reduce risks to human occupants
BREADTH 2: FACADE REDESIGN
Design glazing for worst scenario from site redesign
Goals
  Protect occupants of the building
  Maintain thermal performance
MAE REQUIREMENTS
AE 530 – Computer Modeling of Building Structures
AE 538 – Earthquake Engineering
AE 542 – Building Enclosure Science and Design
STRUCTURAL DEPTH
Reinforced concrete
Maintain flat slab system
Gravity Design
  Use designed OL1 for OL2 - OL4
  Design edge beams
  Design roof structure
Lateral Design
  Ordinarily reinforced concrete shear walls
Progressive Collapse Design
  Satisfy requirements adopted by the U.S. Dept. of Defense
Goals
  Reduce cost of structural system
  Simplify construction

## Slide 11: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
GRAVITY DESIGN
GRAVITY SYSTEM
2 – way flat slab
  Office levels
  Significantly cheaper than existing steel system
  Reduces floor-to-floor height
Perimeter edge beams
  Creates moment frames
  Depth constrained to allowed structure plenum
All columns continued from parking levels through office levels
  2 additional column lines
Check strength of existing column designs
  Higher loads
DESIGN CONSIDERATIONS
Risk Category IV
  Isnow = 1.2
All Concrete f’c = 5000 psi
Façade Load
  Assume 100 psf
Floor to floor height
  9’-0” Floor to ceiling
  17” Clear space in existing Office structure
  Provide 24” below flat slab
  8” slab system
  Result = 11’-8”
  Reduce overall by 7’-8”

## Slide 12: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
GRAVITY DESIGN
DESIGN OF EDGE BEAMS
GSA Design Guide Appendix B.3
  2(DL + 0.5L)
9’-0” Tributary Width
20” Trial Depth (2.5*h)
  Gives sufficient beam/slab ratio
ACI Moment Coefficients
  East – West direction
Frame Analysis
  North – South direction
  Pattern Loading

## Slide 13: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
GRAVITY DESIGN
DESIGN/CHECK OF COLUMNS
GSA Design Guide Appendix B.3
  2(DL + 0.5L)
Live load reduction considered
Spliced at OL1
  “Check” below
  “Design” above
Unbalanced moment from slabs
Spreadsheet
  Typical columns
  Highest load columns
Typically 129% of Original As

## Slide 14: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
LATERAL DESIGN
WIND LOAD
120 MPH (Cat. IV)
Exposure B
GCpi
  Office = 0.18
  Parking = 0.55
Cont. Base Shear
  765 k
  North Blowing
SEISMIC LOAD
Site Class = D
Iseismic = 1.5
SDC = C
R = 5 (ORC Walls)
Cs = 0.0249
Weight = 39,017 k
Base Shear
  972 k
SOIL LOAD

## Slide 15: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
LATERAL DESIGN
ETABS MODEL
All elements modeled
Idealize parking levels
Total height = 91’-4”
Effects of cracked sections
Rigid diaphragms
Columns in-line with walls
Walls
  Membrane elements
  18” x 18” maximum mesh
Seismic loads control
  Extreme torsional irregularity N-S direction

## Slide 16: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
LATERAL DESIGN
SHEAR WALL DESIGN
SW7 – SW12 (Same Design)
  SW7 Worst Case
  Seismic N-S Controls
  Primarily Soil Load
SW1 – SW3 (Same Design)
  SW1 Worst Case
  Seismic N-S Controls
SW5, SW6
  Not in scope
SW4
  Architectural interference
  Seismic E-W Controls

## Slide 17: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
LATERAL DESIGN (SW4)

## Slide 18: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
LATERAL DESIGN (SW4)
SHEAR WALL DESIGN
Openings
  105” Tall
  54” Wide
  Increased Reinforcement
Coupling Beams
  35” Deep
  ACI 318-11 21.9.7
  Diagonal Reinforcement
  Transverse Reinforcement
    Tight Curtain
Increase Boundary Reinforcement
  Intersection w/ SW2 and SW3

## Slide 19: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
FOUNDATION IMPACT
CHECK ON TYPICAL SPREAD FOOTING
Gravity and Lateral Considered
  Free Columns
    Negligible Lateral Influence
  Boundary Columns
    High Lateral Influence
Footing at C-1.5 Checked
  ASD Combo (D + 0.75L + 0.75S) = 1165 k
  11’-0” x 11’-0”
  Assuming 9 Geopiers
Results
  12’-0” x 16’-0” (58% Inc.)
  12 Geopiers (33% Inc.)

## Slide 20: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
PROPRESSIVE COLLAPSE DESIGN
REQUIREMENTS
UFC 4-023-03
  Occupancy Category IV
    Tie Force Method
    Alternative Path Method
    Enhanced Local Resistance
TIE-FORCE METHOD
φRn = φΩAsFy
Load Combo Wf = 1.2D + 0.5L
  Internal Ties (3WfLi)
  Peripheral Ties (6WfLiLp)
  Vertical Ties (ATWf)

## Slide 21: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
PROPRESSIVE COLLAPSE DESIGN
ALTERNATE PATH METHOD
Load Combo [(0.9 or 1.2)D + (0.5L or 0.2S)]
  Increase at “Collapse” Bays (x 1.83)
  Notional Lateral Load
    0.2% of Floor DL
SAP 2000 Model
  Hinge Properties Calculated
    0.03 Radians (LS)
  Cracked Section Properties
  Pinned Base Restraints

## Slide 22: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
PROPRESSIVE COLLAPSE DESIGN
ENHANCED LOCAL RESISTANCE
Occupancy Category IV
  First 2 Stories Above Grade
Double Moment Capacity
RESULTING DESIGN
31” Deep Beams N – S Direction
28” Deep Beams E – W Direction
Limit Aggregate Size

## Slide 23: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
STRUCTURAL DESIGN SUMMARY
SLABS
8” Thick Concrete
Typical Bottom Mat
  #6 @ 12” O.C. N – S
  #6 @ 15” O.C. E – W
EDGE BEAMS
Longitudinal Reinforcement
  Varies #9, #10, #11
Transverse Reinforcement
  #4 @ 5” O.C.
24” Wide
28” – 31” Deep
COLUMNS
24” x 30” Exterior (12 #11 Bars)
Interior Reinforcement Increases
COST COMPARISON
Existing Structure
  $4,127,161
All Concrete Structure
  $4,541,898
Difference
  $414,737
8% Increase
  Progressive collapse design
  Edge beams
  Result = $448,000 Additional Structure Cost

## Slide 24: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
N
N

## Slide 25: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
GLAZING DESIGN
DESIGN PARAMETERS
35’ Standoff Distance
Small Car Bomb
  80 lb. TNT Equivalent
DESIGN GUIDES
ASTM F2248-12
  Equivalent 3s Blast Load
E1300-12a
  Glazing Design Tables
RESULTS
All glass heat strengthened
Occupants Protected
Thermal Performance Not Achieved
  More heat gain in summer
  More heat gain in winter

## Slide 26: PRESENTATION OUTLINE
BUILDING INTRODUCTION
EXISTING STRUCTURE
THESIS PROPOSAL
STRUCTURAL DEPTH
BREADTH 1: SITE REDESIGN
BREADTH 2: FAÇADE REDESIGN (GLAZING)
RESULTS
QUESTIONS
CONCLUSION
Successful design of structure using reinforced concrete
  However, costs $448,000 more
Meets requirements for OC IV Building
Meets requirements of Department of Defense for progressive collapse
Site safety increased, however not ideal
Occupant safety increased
  Lost thermal performance

## Slide 27
QUESTIONS
ACKNOWLEDGEMENTS
AE Faculty
  Dr. Boothby
  Dr. Lepage
  Professor Parfitt
AE Graduate Students
  David Tran
  Ryan Solnosky
Cagley & Associates
  Frank Malits
  Nehemias Iglesias
Halle Companies
  Rich Rounds
DCS Design
  Carmencita Calong
My family, fiancée, and friends
Image Provided By DCS Design