## Slide 1
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
https://www.google.com/maps/place/150+Gamma+Dr/@40.4997521,-79.8681269,18z/data=!4m2!3m1!1s0x8834ecdbc348bd5f:0xd10a14f6b42509a0

## Slide 2
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Background
Location: Pittsburgh, Pennsylvania
Building Use:
          Warehouse Storage
          Laboratory Space
          Offices
Footprint: 74,900 square feet
Ceiling Height:
          Offices: 9’
          Warehouse: 22’ 6”
Renovated: 2012
https://www.google.com/maps/place/150+Gamma+Dr/@40.4997521,-79.8681269,18z/data=!4m2!3m1!1s0x8834ecdbc348bd5f:0xd10a14f6b42509a0

## Slide 3
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Design Conditions
Outdoor Design Conditions
Indoor Design Conditions
 | Summer Design Cooling | Winter Design Heating
OA Dry Bulb (°F) | 89 °F | 2.0 °F
OA Wet Bulb (°F) | 72 °F | .3 °F
 | Offices & Lab | Warehouse & Packaging | Storage & Maintenance
Cooling Set Point | 70 °F | 85 °F | 95 °F
Heating Set Point | 55 °F | 55 °F | 60 °F
Relative Humidity | 45% | - | -

## Slide 4
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Existing Mechanical System
Office/Lab Space
Warehouse and Storage
6 single zone CAV rooftop units (RTUs)
CO2 preheat conditioning option available
CO2 radiant floor cooling and heating
Primarily electric resistance heat
8 air handling units (AHUs)
Makeup air handling unit

## Slide 5
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Annual Load Simulation
Monthly Cooling Load Figure
Chart: Monthly Energy Consumption
| January | February | March | April | May | June | July | August | September | October | November | December
Series 1 | 258272 | 231784 | 263186 | 264398 | 283377 | 285883 | 302073 | 295434 | 278985 | 276424 | 250703 | 261537
Chart: Energy Consumption By Use
| HVAC | Electrical Equipment | Lighting
Energy Consumption Breakdown | 18.3 | 35.7 | 46

## Slide 6
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Annual Load Simulation
Chart: Energy Consumption By Use
| HVAC | Electrical Equipment | Lighting
Energy Consumption Breakdown | 18.3 | 35.7 | 46
Annual Energy Consumption By Use
HVAC:
Lighting:
Electrical Equipment:
Total Annual Energy Consumption:
595,045 kWh
2,657,011 kWh
3,252,057 kWh
6,5041,143 kWh

## Slide 7
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Energy Cost and Consumption
Chart: Electrical Cost by Use
| January | February | March | April | May | June | July | August | September | October | November | December
HVAC | 4085 | 3797 | 5158 | 5493 | 7008 | 8168 | 8181 | 8118 | 7090 | 5918 | 4683 | 4331
Lighting | 13172 | 11786 | 12818 | 12696 | 12976 | 12505 | 13137 | 12794 | 12685 | 13156 | 12360 | 13169
Electrical Equipment | 12156 | 10877 | 11830 | 11718 | 11976 | 11541 | 12124 | 11807 | 11707 | 12142 | 11407 | 12153
Annual Cost per Unit Floor Area
HVAC:
Lighting:
Electrical Equipment:
Total Annual Energy Cost:
$0.96/ft2
$2.04/ft2
$1.89/ft2
$366,744

## Slide 8
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Variable Refrigerant Flow System
System Components
Advantages
Disadvantages
Expensive first costs
Requires DOAS system
Lower energy costs
Lower CO2e emissions
Simultaneous heating and cooling
Precise and occupant control capabilities
Outdoor/Indoor Condensing Unit
3 pipe system (suction, liquid, discharge gas)
Mode Change Unit (MCU)
2 pipe system from MCU to fan coil unit
Indoor fan coil units
http://y.asi.ph/note/commissioning-daikin-vrv-systems/

## Slide 9
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
VRF System Layout
System Layout Restrictions
Key
VRF System 1
VRF System 2
VRF System 3
Piping Length – 656 feet maximum
External Static Pressure – 1” maximum
Condensing Unit Elevation – 360 feet maximum

## Slide 10
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Condensing Unit Quantity
Samsung DVM S Series Condensing Unit Requirements
Number of Condensing Units Needed | One | Two | Three
Size (tons) | 6-12 | 14-24 | 26-36
VRF System | 1 | 2 | 3
Size (tons) | 11.5 | 17.2 | 12.5
Number of Condensing Units Needed | One | Two | Two

## Slide 11
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Indoor Fan Coil Unit Selection
1 Way Cassette Terminal Unit
4 Way Cassette Terminal Unit
High Static Pressure (HSP) Duct Unit
1-Way Cassette Terminal Unit
Located at edges of room ceiling
Diffuses in one direction
4-Way Cassette Terminal Unit
Located in central area of ceiling
Distributes air in four directions
High Static Pressure Duct Unit
Up to .99 in wg. external static pressure
Can condition multiple spaces at a time
Source: Samsung DVM S Series Catalog
Source: Samsung DVM S Series Catalog
Source: Samsung DVM S Series Catalog

## Slide 12
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
VRF System Selection
VRF System 1
12 ton Outdoor Condensing Unit (1)
Mode Change Units (3)
4 Way Cassette FCU (6)
1 Way Cassette FCU (9)
CU-1

## Slide 13
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
VRF System Selection
VRF System 2
6 ton Outdoor Condensing Unit (1)
10 ton Outdoor Condensing Unit (1)
Mode Change Units (4)
4 Way Cassette FCU (12)
1 Way Cassette FCU (7)

## Slide 14
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
VRF System Selection
VRF System 3
6 ton Outdoor Condensing Unit (1)
10 ton Outdoor Condensing Unit (1)
Mode Change Units (3)
4 Way Cassette FCU (3)
1 Way Cassette FCU (4)
High Static Pressure Unit (2)

## Slide 15
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Dedicated Outside Air System
Semco FV-2000 Fresh Air Preconditioner
3 Angstrom Total Energy Wheel
Parallel system to VRF system
Manages humidification and de-humidification
 | Airflow (cfm) | Ext. Static Pressure (in wg.) | Motor Brake Horsepower | Fan Speed (RPM)
Supply Air | 1,250 | 1.50 | 1.00 | 1723
Exhaust Air | 1,175 | .75 | .64 | 1413
Design Conditions: Cooling Season
Outdoor Airstream
Supply Airstream
Return Airstream
Exhaust Airstream
Dry Bulb (°F) : 95.0
Wet Bulb (°F): 75.0
Enthalpy (BTU/lb): 38.4
Dry Bulb (°F) : 90.8
Wet Bulb (°F): 72.5
Enthalpy (BTU/lb): 36.1
Dry Bulb (°F) : 75.0
Wet Bulb (°F): 62.0
Enthalpy (BTU/lb): 27.8
Airflow (CFM): 1,175
Dry Bulb (°F) : 80.2
Wet Bulb (°F): 65.7
Enthalpy (BTU/lb): 30.5
Airflow (CFM): 1,250
Source: Semco FV 2000 Catalog

## Slide 16
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Dedicated Outside Air System
Design Conditions: Cooling Season
Outdoor Airstream
Supply Airstream
Return Airstream
Exhaust Airstream
Dry Bulb (°F) : 95.0
Wet Bulb (°F): 75.0
Enthalpy (BTU/lb): 38.4
Dry Bulb (°F) : 90.8
Wet Bulb (°F): 72.5
Enthalpy (BTU/lb): 36.1
Dry Bulb (°F) : 75.0
Wet Bulb (°F): 62.0
Enthalpy (BTU/lb): 27.8
Airflow (CFM): 1,175
Dry Bulb (°F) : 80.2
Wet Bulb (°F): 65.7
Enthalpy (BTU/lb): 30.5
Airflow (CFM): 1,250
Efficiency and Static Pressure Loss
Sensible Supply Efficiency: 74%
Latent Supply Efficiency: 74%
Supply Air Pressure Loss: .36
Exhaust Air Pressure Loss: .33

## Slide 17
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Controls
BACnet Gateway Building Management System
Can connect up to 256 indoor units/16 outdoor units
Weekly/Daily Scheduling
Temperature limitations
ERV operation mode and fan speed
Zone Management
Occupant Controls
MWR-WE10N Wired Remote Controller
Can control up to 16 indoor units and ERV
Operation mode
Temperature setting (limited by BACnet)
ERV operation and fan speed (limited by BACnet)

## Slide 18
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Cost Analysis
Chart: VRF System Monthly HVAC Energy Consumption
| January | February | March | April | May | June | July | August | September | October | November | December
VRF Systems | 1573 | 1348 | 2130 | 2404 | 4067 | 5855 | 6408 | 6499 | 4457 | 2898 | 1768 | 1467
Chart: VRF Zone Annual Energy Consumption By Use
| HVAC | Electrical Equipment | Lighting
Energy Consumption Breakdown | 9 | 40 | 50

## Slide 19
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Cost Analysis
Chart: VRF System Zones Electrical Cost by Use
| January | February | March | April | May | June | July | August | September | October | November | December
HVAC | 531 | 478 | 600 | 625 | 837 | 1046 | 1111 | 1130 | 875 | 694 | 549 | 518
Lighting | 2047 | 1857 | 1994 | 1976 | 2004 | 1926 | 2012 | 1963 | 1960 | 2037 | 1933 | 2048
Electrical Equipment | 1068 | 969 | 1041 | 1031 | 1046 | 1005 | 1050 | 1025 | 1023 | 1063 | 1009 | 1069
Annual HVAC Cost Per Unit Area:
$0.71/ft2
Total Annual HVAC Energy Cost:
$9,001

## Slide 20
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Energy Consumption Comparison
Original Design Annual HVAC Energy Consumption:
85,148 kWh
VRF System Annual HVAC Energy Consumption:
72,316 kWh
Difference:
12,832 kWh
Chart: Monthly HVAC Energy Consumption
| January | February | March | April | May | June | July | August | September | October | November | December
Original | 2630 | 2493 | 4922 | 5673 | 8943 | 11782 | 12802 | 12865 | 9381 | 6501 | 4016 | 3140
VRF System | 4244 | 3759 | 4801 | 4988 | 6737 | 8439 | 9078 | 9170 | 7041 | 5568 | 4353 | 4138

## Slide 21
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Energy Cost Comparison
Original Design Annual HVAC Energy Cost:
$16,416
VRF System Annual HVAC Energy Cost:
$9,001
Difference:
$7,415
Chart: Monthly HVAC Energy Cost
| January | February | March | April | May | June | July | August | September | October | November | December
Original | 914 | 971 | 1112 | 1183 | 1563 | 1902 | 2016 | 2026 | 1617 | 1279 | 1005 | 928
VRF System | 531 | 478 | 600 | 625 | 837 | 1046 | 1117 | 1130 | 875 | 694 | 549 | 518

## Slide 22
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Mechanical First Costs Comparison
 | Materials | Labor | Total
Original HVAC System | $144,663.88 | $79,733.00 | $222,396.88
VRF System | $327,702.26 | $20,690.81 | $348,393.07
Difference | -$178,038.38 | $59,042.19 | -$118,996.19
Original HVAC vs. VRF System First Costs
Materials Difference: +118%
Labor Difference: -74%
Total First Cost Difference: +51.8%

## Slide 23
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Payback Period
FCO= First Cost of Original HVAC System
AECO= Annual Energy Cost of Original HVAC System
FCVRF= First Cost of Original VRF System
AECVRF= Annual Energy Cost of VRF HVAC System
X= Payback Period in years
Equation
FCO + (AECO * X) = FCVRF + (AECVRF * X)
$229,396 + ($16,416*X) = $348,393.07 + (9001 * X)
$118996 = $7415 * X
Variables
Payback Period
X= 16.04 years

## Slide 24
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Emissions Comparison

## Slide 25
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Acoustical Breadth Investigation
Recommended Noise Criterion - NC
 | Recommended NC Rating | Equivalent Sound Level dBA
Open-Plan Offices | 35-40 | 45-50
Private Offices | 30-35 | 40-45
Conference Rooms | 25-30 | 35-40
KEY
Private Offices
Conference Rooms
Open Plan
Offices

## Slide 26
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Acoustical Breadth Investigation
Existing Mechanical Conditions
5 Ton Carrier 50TCD06 Rooftop Unit
1” Fiberglass Insulation
Room Dimensions : 34’x26’x8’
Measure SPL to nearest diffuser
Existing Mechanical NC Rating
NC-46
~ 48 dBA
 | Sound Power Level, dB (re 10^-12 W) |  |  |  |  |  | 
Octave Band Frequency, HZ | 63 | 125 | 250 | 500 | 1000 | 2000 | 4000
Discharge | 85.8 | 84.3 | 80.5 | 78.7 | 76.4 | 72.7 | 68.3

## Slide 27
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Acoustical Breadth Investigation
Existing Mechanical NC Rating
NC-46
~ 48 dBA
Recommended Noise Criterion - NC
 | Recommended NC Rating | Equivalent Sound Level dBA
Open-Plan Offices | 35-40 | 45-50
Private Offices | 30-35 | 40-45
Conference Rooms | 25-30 | 35-40

## Slide 28
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Acoustical Breadth Investigation
Proposed Mechanical Conditions
Recommended Noise Criterion - NC
Samsung DMV AM024FN4dCH/AA 4 Way Cassette Fan Coil Units
Room Dimensions : 34’x26’x8’
 | Sound Power Level, dB (re 10^-12 W) |  |  |  |  |  | 
Octave Band Frequency, HZ | 63 | 125 | 250 | 500 | 1000 | 2000 | 4000
Discharge | 40.1 | 37.2 | 36.4 | 33.0 | 29.7 | 27.3 | 22.6
NC-25
~ 32 dBA

## Slide 29
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Acoustical Breadth Investigation
Recommended Noise Criterion - NC
NC-25
~ 32 dBA
Recommended Noise Criterion - NC
 | Recommended NC Rating | Equivalent Sound Level dBA
Open-Plan Offices | 35-40 | 45-50
Private Offices | 30-35 | 40-45
Conference Rooms | 25-30 | 35-40

## Slide 30
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Conclusion
Variable Refrigerant Flow System
First Costs – 51% more expensive than original
Annual Costs – 45% cheaper than original system
Payback Period – 16 years (uneconomical)
Emissions – 13% less annually than original
Improve occupant comfort
Acoustical Invesitgation
Original Design – did not meet recommended NC Ratings for office spaces
Potential for rumbly HVAC noise
VRF Design – met all recommended NC Rating and dBA values

## Slide 31
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Acknowledgements
AE Staff and Faculty
Marc Portnoff
Jonathan Iams
Joel Butler
Dan Gardner
My friends and family

## Slide 32
Introduction
Existing Mechanical System
Variable Refrigerant Flow System
Cost Analysis
Emissions Analysis
Acoustical Design
Conclusion
Alexander Radkoff
Mechanical Option | Spring 2014
Advisor: Dr. Stephen Treado
123 Alpha Drive
Pittsburgh,
Pennsylvania
Questions?