## Slide 1
La Jolla Commons
Phase II Office Tower
San Diego, California
Alyssa Stangl | Structural Option
Faculty Advisor | Dr. Hanagan
  Photos Provided Courtesy of HINES

## Slide 2
  Location | San Diego, California – SDC D
  13 Stories + Penthouse | 198’ – 8”
  2 Levels | Underground parking
  462,301 GSF
  Design-Bid-Build
  Construction Dates | April 2012 – May 2014
  Building Cost | $78,000,000
La Jolla Commons Office Tower
Building Introduction
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
San Diego, CA

## Slide 3
  Owner | Hines
  Tenant | LPL Financial
  Architect | AECOM
  Structural Engineer | Nabih Youssef Associates
La Jolla Commons Office Tower
Project Team
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Photo Provided Courtesy of HINES

## Slide 4
  Large open floor plans
  Office use only
  Similar architecture to LJC Tower I
  198’-8” height limited by FAA
  LEED-CS Gold & NetZero
La Jolla Commons Office Tower
Architectural Overview
128 ‘ – 8”
315’ – 0”
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N
  Image from Project Documents Provided Courtesy of HINES

## Slide 5
La Jolla Commons Office Tower
Architectural Overview
Core – Elevators, Stairs, Mech
Office Space
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N
  Large open floor plans
  Office use only
  Similar architecture to LJC Tower I
  198’-8” height limited by FAA
  LEED-CS Gold & NetZero
  Image from Project Documents Provided Courtesy of HINES

## Slide 6
La Jolla Commons Office Tower
Architectural Overview
Tower II
Tower I
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Large open floor plans
  Office use only
  Similar architecture to LJC Tower I
  198’-8” height limited by FAA
  LEED-CS Gold & NetZero
  Photo Provided Courtesy of HINES

## Slide 7
La Jolla Commons Office Tower
Existing Structural Overview
  Gravity System
    Mat foundation
    Floor System
  Lateral System
    Shear Walls
    Collectors
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N
  Image from Project Documents Provided Courtesy of HINES

## Slide 8
La Jolla Commons Office Tower
Existing Structural Overview
  Gravity System
    Mat foundation
    Floor System
      Two-Way, Flat Plate Concrete Slab
      10” – 14” Thickness
      18” Spandrel Beam
  Lateral System
    Shear Walls
    Collectors
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N
  Image from Project Documents Provided Courtesy of HINES

## Slide 9
La Jolla Commons Office Tower
Existing Structural Overview
  Gravity System
    Foundation
    Floor System
  Lateral System
    Shear Walls
      Existing Torsional Irregularity
    Collectors
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 10
La Jolla Commons Office Tower
Existing Structural Overview
  Gravity System
    Foundation
    Floor System
  Lateral System
    Shear Walls
    Collectors
      N-S Direction at Lower Levels
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N
  Image from Project Documents Provided Courtesy of HINES

## Slide 11
La Jolla Commons Office Tower
Design Scenario
Proposed Solution
  Redesign the building in steel
  Modify lateral system to eliminate existing torsional irregularity
  Determine Impact
    Architecture
    Serviceability – Walking induced vibrations
    Cost and schedule
  Use original column locations
  Determine configuration of composite steel beams to control vibrations
  Add steel moment frames to building perimeter to control torsion
  Determine floor-to-ceiling height impact
  Compare costs and schedules
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 12
La Jolla Commons Office Tower
Gravity Redesign
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 13
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
La Jolla Commons Office Tower
Preliminary Vibrations Analysis
Deck Configuration for Vibration Control | 
Concrete Strength | 3000 psi
Steel Grade | 50
Deck Type | 1.5VLR20
Topping (in) | 4.25
LW/NW? | LW
Total Slab Thickness (in) | 5.75
Class | 4
Select C1 | 0.413
Select C2 | 0.019
Evaluate C1 + C2 | 0.432
C1 + C2 < 0.5? | GOOD
  Vibrations due to human excitation
  Control peak acceleration of the bay
Design Selection:
  1.5VLR20
  4.25” LW Topping
  7.5’ – 8’ beam spacing
  Source: The Preliminary Assessment for Walking-Induced Vibrations in Office Environments by Dr. Linda Hanagan and Taehoo Kim

## Slide 14
  Which direction to span infill beams?
    Short
    Long
  Long Direction Selected
La Jolla Commons Office Tower
Gravity System Layout
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 15
  Which direction to span infill beams?
    Short
    Long
  Long Direction Selected
La Jolla Commons Office Tower
Gravity System Layout
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 16
  Which direction to span infill beams?
    Short
    Long
  Long Direction Selected
La Jolla Commons Office Tower
Gravity System Layout
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
Infill Beam Comparison |  | 
 | Steel Weight (lbs) | Number of Members
Long Direction | 212936 | 155
Short Direction | 179608 | 225

## Slide 17
La Jolla Commons Office Tower
Gravity System Layout
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N

## Slide 18
La Jolla Commons Office Tower
RAM Gravity Model
  RAM SS used to develop gravity designs
    Composite steel beams
    Steel columns
  Several designs verified by hand calculations
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
Gravity Loads |  | 
 | Dead (PSF) | Live (PSF)
Core | 90 | 250
Lease Space | 90 | 80

## Slide 19
La Jolla Commons Office Tower
Beam Designs
  Common Member Sizes:
    W21x44 (28) infill exterior bays
    W24x62 (32) infill interior bays
    W21x50 (18) exterior girder
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N

## Slide 20
La Jolla Commons Office Tower
Column Designs
  Spliced every 2 stories
  Each column line has consistent column depth
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 21
La Jolla Commons Office Tower
Column Designs
  Spliced every 2 stories
  Each column line has consistent column depth
    Exterior Column Line
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
W10X33
W10X88

## Slide 22
La Jolla Commons Office Tower
Column Designs
  Spliced every 2 stories
  Each column line has consistent column depth
    Exterior Column Line
    Interior Column Line
W14X43
W14X193
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 23
La Jolla Commons Office Tower
Final Vibrations Analysis
  AISC Design Guide 11 analysis on a typical bay for walking induced vibrations
  Determine combined panel weight and natural frequency to determine bay peak acceleration
    P0 = 65 lb
    = 0.03
    a0/g < 0.5%
From AISC DG 11 – Table 4.1
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 24
La Jolla Commons Office Tower
Lateral Redesign
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 25
La Jolla Commons Office Tower
Lateral System
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Reduced building weight
   Seismic loads decreased
  Building height unchanged
   Wind loads unchanged
  Seismic controls
Base Shear (Kip) |  |  |  | 
 | Wind N-S | Wind E-W | Seismic N-S | Seismic E-W
Concrete | 583 | 1615 | 7698 | 7698
Steel | 583 | 1615 | 4935 | 4408

## Slide 26
La Jolla Commons Office Tower
Existing Lateral System Layout
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
COR
COM
Eccentricity = 10’
N

## Slide 27
La Jolla Commons Office Tower
New Lateral System Layout
COM
COR
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
N
Eccentricity = 1’

## Slide 28
La Jolla Commons Office Tower
RAM Model
  Rigid diaphragms
  Wall shell elements neglect out of plane stiffness
  Stiffness reduction based on ACI 318-11
  Panel zone deformations considered
  Base constraints
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 29
La Jolla Commons Office Tower
Special Moment Frames
  Special moment frames required by ASCE 7-10
    SDC D
    198’ > 65’
  Designed to be “clean column”
    Strong panel zone
  Strength and joint optimizations for seismic
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 30
La Jolla Commons Office Tower
Special Moment Frames
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
Notes:   Special attention to connection detailing
  No openings in beam at hinge locations
  Force elasticity into beams – Strong Panel Zone
    Connection design
    Reduce beam section at hinge zone
  75% of elastic deformation in beam hinges
  Requirements for Highly Ductile members

## Slide 31
La Jolla Commons Office Tower
Special Moment Frames
FRAME 1
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
Levels 3-5

## Slide 32
La Jolla Commons Office Tower
Special Concrete Shear Walls
  Thickness not reduced to control drift
  Reinforcing redesigned for reduced loads
    According to ACI 318-11 Ch. 21
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 33
La Jolla Commons Office Tower
Special Concrete Shear Walls
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Shear Wall U Level 2– Reinforcing redesign
    7000 PSI NW Concrete, 18” Thick
H = #6 @ 9” O.C.
V = #6 @ 9” O.C.
One curtain only
  Image from Project Documents Provided Courtesy of HINES

## Slide 34
La Jolla Commons Office Tower
Architecture Breadth
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Photo Provided Courtesy of HINES

## Slide 35
La Jolla Commons Office Tower
Floor-to-Ceiling Height
  Building height limited to 198’-8” by FAA
  Steel creates a deeper structural system than concrete
  Loss of floor-to-ceiling space
198’ – 8”
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Photo Provided Courtesy of HINES

## Slide 36
La Jolla Commons Office Tower
Floor-to-Ceiling Height
  Concrete
  Steel
1’-6” Decrease in floor-to-ceiling height
10’-8”
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
9’-2”

## Slide 37
La Jolla Commons Office Tower
Construction Breadth
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Photo Provided Courtesy of HINES

## Slide 38
La Jolla Commons Office Tower
Concrete System Cost
  Cost information provided by Hines
  Concrete chosen because it was cheaper than steel system
  Approximately $61 per SF
Original Concrete Structure Cost Summary | 
Cost Per SF | $ 61.46
Structural Square Footage | 462,301 SF
% General Conditions | 14%
Total Original Structure Cost | $ 28,413,000
General Conditions Cost | $ 3,978,000
Original Structure Cost w/ out General Conditions | $ 24,435,000
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 39
La Jolla Commons Office Tower
Steel System Cost
  Based on cost information from RS Means 2009
  Approximately $65 per SF
Total Steel Structure Cost (2009 RS Means) | 
Item | Cost
Concrete on Metal Deck | $ 3,050,000
Structural Steel Framing | $ 9,052,000
Shear Walls | $ 4,310,000
Foundation Walls | $ 1,929,000
Lower Level Concrete Slabs | $ 2,796,000
Lower Level Concrete Columns | $ 198,000
Mat Foundation | $ 4,055,000
Total Cost | $ 25,391,000
Final Modified Cost | $ 30,072,000
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 40
La Jolla Commons Office Tower
Cost Comparison
  23 % Increase in cost for steel system
  Validates original decision by designers to design structure in concrete
Final Cost Comparison | 
Original Concrete Structure Cost | $ 24,435,000
New Steel Structure Cost | $ 30,072,000
% Increase in Cost | 23%
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions

## Slide 41
La Jolla Commons Office Tower
Concrete System Schedule
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Schedule information provided by Hines
  Superstructure duration | 240 days
  Image Extracted from Project Schedule Provided Courtesy of HINES

## Slide 42
La Jolla Commons Office Tower
Steel System Schedule
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Schedule produced in Microsoft Project
  Durations from RS Means 2009
  Superstructure duration | 230 days

## Slide 43
La Jolla Commons Office Tower
Schedule Comparison
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Only 2 weeks time savings
  Not worth the 23% cost increase
  If time savings were more significant, cost increase may have been offset

## Slide 44
La Jolla Commons Office Tower
Conclusions
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Designed a feasible steel gravity system with vibration reducing characteristics
  Designed special steel moment frames
  Eliminated torsional irregularity
  Reduced floor-to-ceiling heights
  Increased cost for steel structure is not offset by reduction in project schedule
  Photo Provided Courtesy of HINES

## Slide 45
La Jolla Commons Office Tower
Acknowledgements
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Special Thanks to:
  Hines
  Nabih Youssef Associates
  AE Faculty | especially Dr. Linda Hanagan & Prof. Sustersic
  Benjamin Barben
  My loving family, boyfriend, friends, and classmates
  Photo Provided Courtesy of HINES

## Slide 46
La Jolla Commons Office Tower
Questions and Comments?
Building Introduction
Design Scenario and Proposed Solution
Gravity Redesign
  Preliminary Vibrations Analysis and Layout
  Beam and Column Designs
  Final Vibrations Analysis
Lateral Redesign
  Layout
  Moment Frames
  Shear Walls
Architecture Breadth
Construction Breadth
Conclusions
  Photo Provided Courtesy of HINES

## Slide 47
La Jolla Commons Office Tower
Appendix Slides
Architecture Breadth
Shear Wall Modeling
Model Verification
Dual Systems Check
Lateral System Verification
Vibrations Analysis

## Slide 48
La Jolla Commons Office Tower
Architecture Breadth
Appendix List

## Slide 49
La Jolla Commons Office Tower
Floor-to-Ceiling Height
  Building height limited to 198’-8” by FAA
  Steel creates a deeper structural system than concrete
  Loss of floor-to-ceiling space
198’ – 8”
Appendix List

## Slide 50
La Jolla Commons Office Tower
Floor-to-Ceiling Height
  Concrete
  Steel
1’-6” Decrease in floor-to-ceiling height
Appendix List

## Slide 51
La Jolla Commons Office Tower
Fire Protection Breadth
Required Fire-Resistance Ratings |  | 
Element | Construction Type | Required Rating (hours)
Primary Floor Framing Members | Type 1B | 2
Secondary Floor Framing Members | Type 1B | 2
Structural Columns | Type 1A | 3
Appendix List

## Slide 52
La Jolla Commons Office Tower
Fire Protection Breadth
1.5” of SFRM
Required Spray Fireproofing Thickness |  |  |  |  | 
722.5.2.2.1 Requirements |  |  |  |  | 
Min W/D for Substitute Beam: | 0.37 | OK |  |  | 
Min Thickness of Protection: | 0.375 | in |  |  | 
Unrestrained/restrained? | Unrestrained (to be conservative) |  |  |  | 
Min Fire Rating: | 1 hour |  |  |  | 
Required Fire Rating: | 2 hour |  |  |  | 
Minimum Beam Size: | W12x14 |  |  |  | 
Heated Perimeter: | 0.405 |  |  |  | 
Assembly Tested | Min Beam Size | h1 | W1/D1 | W2/D2 | h2
N708 | W8x28 | 1.00 | 0.819 | 0.405 | 1.412
Appendix List

## Slide 53
La Jolla Commons Office Tower
Fire Protection Breadth
1. The outer layer must be 5/8 inches thick. The inner layers will be 5/8 inch thick wall board as well. The wallboard is
installed without any horizontal joints. 1 inch long self-drilling screws shall be spaced as required for the installation of
the first layer of wall board.
2. 28 MSG galvanized metal corner bead
3. 18 SWG annealed wire, space 6 inches from each end and at 1’-9” intervals
4. May be finished with 3/32” thick gypsum veneer plaster. Joints reinforced.
5. Laminated with joint cement.
6. 1 inch long self-drilling screws spaced at 12” center to center
7. Minimum column size of W10X49. 9/16 flange thickness and 5/16 inch web thickness. 14.4 square inch area.
Appendix List

## Slide 54
La Jolla Commons Office Tower
Fire Protection Breadth
Figure 3.2 - 7 | Resistance between Occupancies – IBC 2012 Table 707.3.10
  4.25 LW topping provided
  Adequate for 2 hour fire resistance between levels
Appendix List

## Slide 55
La Jolla Commons Office Tower
Fire Protection Breadth
Appendix List

## Slide 56
La Jolla Commons Office Tower
Shear Wall Modeling
Appendix List

## Slide 57
La Jolla Commons Office Tower
Shear Wall Modeling Method
  Shell elements connected at nodes caused an irregular distribution of torsional forces within the wall core
  Bentley suggested disconnecting the shear walls and adding gravity framing elements to eliminate a “framing tables” error
  Does not count on flanged walls to take out of plane loads or to help in flexure
  Eliminated odd torsionally anomaly
Appendix List

## Slide 58
La Jolla Commons Office Tower
Model Verification
Appendix List

## Slide 59
La Jolla Commons Office Tower
Model Verification
Model Verification Summary |  | 
 | % Error X-Direction | % Error Y-Direction
Center of Mass | 0.284% | 1.265%
Center of Rigidity | 2.813% | 1.681%
Floor Mass | 11% | 
Seismic Loads | 15% | 
Wind Loads | 0.25% | 3.31%
2D Analysis | 10 - 20 % | 
Appendix List

## Slide 60
La Jolla Commons Office Tower
Dual System Check
Appendix List

## Slide 61
La Jolla Commons Office Tower
Dual System Check
Dual System Check |  |  | 
X-Direction Direct Shear |  |  | 
Item | Shear (kip) | % of Total Shear | Dual System?
Frame 1 | 595.21 | 18.27% | No
Frame 2 | 643.37 | 19.74% | No
Shear Walls | 2020.00 | 61.99% | -
Total Shear | 3258.58 kip |  | 
Y-Direction Direct Shear |  |  | 
Item | Shear (kip) | % of Total Shear | Dual System?
Frame 3 | 35.61 | 1.18% | No
Frame 4 | 32.41 | 1.08% | No
Shear Walls | 2941.00 | 97.74% | -
Total Shear | 3009.02 kip |  | 
Appendix List

## Slide 62
La Jolla Commons Office Tower
Lateral System Verification
Appendix List

## Slide 63
La Jolla Commons Office Tower
Lateral System Verification
  Drifts for wind and seismic were verified to meet code and industry standard requirements (Cd=5, R=6)
  Torsional analysis was performed at each story under the different seismic load cases and found to no longer have an irregularity
  Stability coefficients were verified
  Overturning moment was checked under the controlling load case
Wind Displacement Determination |  |  |  | 
Load Case | X - Deflection (in) | Y - Deflection (in) | L/400 (in) | Pass/Fail?
Wind_ASCE710_1_X | 1.91 | 0.00 | 5.940 | Pass
Wind_ASCE710_1_Y | 0.00 | 2.11 | 5.940 | Pass
Wind_ASCE710_2_X+E | 1.43 | -0.01 | 5.940 | Pass
Wind_ASCE710_2_X-E | 1.43 | 0.01 | 5.940 | Pass
Wind_ASCE710_2_Y+E | 0.01 | 1.68 | 5.940 | Pass
Wind_ASCE710_2_Y-E | -0.01 | 1.49 | 5.940 | Pass
Wind_ASCE710_3_X+Y | 1.43 | 1.58 | 5.940 | Pass
Wind_ASCE710_3_X-Y | 1.43 | -1.58 | 5.940 | Pass
Wind_ASCE710_4_X+Y_CW | 1.07 | 1.11 | 5.940 | Pass
Wind_ASCE710_4_X+Y_CCW | 1.08 | 1.27 | 5.940 | Pass
Wind_ASCE710_4_X-Y_CW | 1.07 | -1.26 | 5.940 | Pass
Wind_ASCE710_4_X-Y_CCW | 1.08 | -1.10 | 5.940 | Pass
Appendix List

## Slide 64
La Jolla Commons Office Tower
  Drifts for wind and seismic were verified to meet code and industry standard requirements (Cd=5, R=6)
  Torsional analysis was performed at each story under the different seismic load cases and found to no longer have an irregularity
  Stability coefficients were verified
  Overturning moment was checked under the controlling load case
Seismic Story Drift Check |  |  |  |  |  | 
Level | Level Height (ft) | Cd*δx |  | Allowable Drift (in) | Pass/Fail? | 
 |  | X-Direction | Y-Direction |  | X-Direction | Y-Direction
PH Roof | 24.33 | 5.15 | 2.04 | 5.839 | Pass | Pass
PH | 14.5 | 3.08 | 1.22 | 3.480 | Pass | Pass
13 | 14 | 2.83 | 1.02 | 3.360 | Pass | Pass
12 | 14 | 2.87 | 1.01 | 3.360 | Pass | Pass
11 | 14 | 2.89 | 1.00 | 3.360 | Pass | Pass
10 | 14 | 2.89 | 0.97 | 3.360 | Pass | Pass
9 | 14 | 2.85 | 0.93 | 3.360 | Pass | Pass
8 | 14 | 2.76 | 0.88 | 3.360 | Pass | Pass
7 | 14 | 2.62 | 0.82 | 3.360 | Pass | Pass
6 | 14 | 2.41 | 0.74 | 3.360 | Pass | Pass
5 | 14 | 2.13 | 0.64 | 3.360 | Pass | Pass
4 | 14 | 1.76 | 0.53 | 3.360 | Pass | Pass
3 | 14 | 1.29 | 0.40 | 3.360 | Pass | Pass
2 | 15 | 0.78 | 0.27 | 3.600 | Pass | Pass
Overall Displacement= |  | 36.32 | 12.46 |  |  | 
Appendix List

## Slide 65
La Jolla Commons Office Tower
Lateral System Verification
Check for Torsional Irregularities X Direction |  |  |  |  | 
Level | δA | δB | δavg | δmax | Does a torsional irregularity exist?
PH | 0.6268 | 0.6269 | 0.63 | 0.6269 | No
Level 13 | 0.5762 | 0.5764 | 0.58 | 0.5764 | No
Level 12 | 0.5846 | 0.5847 | 0.58 | 0.5847 | No
Level 11 | 0.5887 | 0.5888 | 0.59 | 0.5888 | No
Level 10 | 0.5877 | 0.5878 | 0.59 | 0.5878 | No
Level 9 | 0.5788 | 0.5789 | 0.58 | 0.5789 | No
Level 8 | 0.5614 | 0.5615 | 0.56 | 0.5615 | No
Level 7 | 0.5320 | 0.5321 | 0.53 | 0.5321 | No
Level 6 | 0.4901 | 0.4902 | 0.49 | 0.4902 | No
Level 5 | 0.4330 | 0.4331 | 0.43 | 0.4331 | No
Level 4 | 0.3582 | 0.3582 | 0.36 | 0.3582 | No
Level 3 | 0.2116 | 0.2637 | 0.24 | 0.2637 | No
  Drifts for wind and seismic were verified to meet code and industry standard requirements (Cd=5, R=6)
  Torsional analysis was performed at each story under the different seismic load cases and found to no longer have an irregularity
  Stability coefficients were verified
  Overturning moment was checked under the controlling load case
Appendix List

## Slide 66
La Jolla Commons Office Tower
Lateral System Verification
Building Resisting Moment |  | 
Worst Case Resistance - Y Direction |  | 
Total Building Weight = | 82296 | kip
Moment Arm = | 57.5 | ft
Factory of Safety= | 0.67 | 
Mresisting = | 3170446 | ft-k
Worst Case Moment for Building Overturning | 
Seismic Y Direction - Load Case: Y + YET | 
381110 | ft-k
Check Overturning |  | 
Worst Case Resistance - Y Direction |  | 
Overturning Moment = | 381,110 | ft-kip
Resisting Moment = | 3,170,446 | ft-kip
Okay? | Pass | 
  Drifts for wind and seismic were verified to meet code and industry standard requirements (Cd=5, R=6)
  Torsional analysis was performed at each story under the different seismic load cases and found to no longer have an irregularity
  Stability coefficients were verified
  Overturning moment was checked under the controlling load case
Appendix List

## Slide 67
La Jolla Commons Office Tower
Vibrations Analysis
Appendix List

## Slide 68
La Jolla Commons Office Tower
Vibrations Analysis
  LL = 11 PSF
  Superimposed DL = 40 PSF
  Concrete weight = 50 pcf (Lightweight)
  Floor thickness = 5.75”
  1.5VLR20 with 4.25” LW topping
  P0 = 65lb
  β = 0.03
  a0/g = 0.5%
  Beam Properties:
    Wj = 153 kip
    fj = 4.39 Hz
    Wg = 205.3 kip
    fg = 4.86 Hz
  Combined Mode Properties:
    fn = 3.36 Hz
    Wtotal = 174.5 kip
  ap/g = 0.38%
  ap/g < a0/g
Appendix List