## Slide 1
Jackson Crossing
Alexandria, Virginia
Michael Bologna
Structural Option
Advisor: Dr. Linda M. Hanagan
The Pennsylvania State University
Spring 2016

## Slide 2
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Introduction
General Building Information
Existing Gravity System
Existing Lateral System

## Slide 3
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Introduction
General Building Information
Existing Gravity System
Existing Lateral System
Design Team
Owner: AHC, Inc.
CM: Harkins Builders, Inc.
Architect: Bonstra | Haresign Architects, LLP
Structural: Rathgeber and Goss Associates
Civil: VIKA, Virginia, LLC
MEP: Metropolitan Engineering, Inc.

## Slide 4
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Introduction
General Building Information
Existing Gravity System
Existing Lateral System
▪ North Elevation

## Slide 5
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Introduction
General Building Information
Existing Gravity System
Existing Lateral System
Existing Gravity System
4 Floors of wood framing
  Rests on second floor podium slab
▪ Second Floor Plan
▪ First Floor Plan
Yellow – Supporting First Floor
Green – Supporting Second Floor
Purple – Supporting Both Floors
Blue – Concrete Beams

## Slide 6
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Introduction
General Building Information
Existing Gravity System
Existing Lateral System
▪ Concrete Shear Walls at First Floor
▪ CMU Shear Walls on Typical Floor Plan
▪ Wood Shear Walls on Typical Floor Plan

## Slide 7
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Problem Statement/Goal
Reduce amount of transfer members and the structural floor depth

## Slide 8
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams

## Slide 9
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
N
▪ Location of Columns on Typical Plan
▪ Columns not continuous to Roof in purple
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams

## Slide 10
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
N
▪ Location of Columns on Typical Plan
▪ Columns not continuous to Roof in purple
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Initial Column Dimension
Chose to base off of compressive strength, φPn
Pu for worst column equal to 525.1k
Need Ag=198.5in2
Initial Column Size:
14” by 14”

## Slide 11
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
N
▪ Location of Columns on Typical Plan
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Designed Columns
Column 1
Pu=525k
Mu1=30 k-ft
Mu2=10 k-ft
Column 2
Pu=260k
Mu1=2 k-ft
Mu2=11 k-ft
Column 1
Column 2

## Slide 12
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Column 1
14” by 14”
5,000 psi
Longitudinal Bars
  (4) #8
  1.61% Reinforcement
Stirrups
  #3 Ties
  14” o.c. (Maximum stirrup spacing)
Column 1

## Slide 13
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Column 2
14” by 14”
5,000 psi
Longitudinal Bars
  (4) #7
  1.22% Reinforcement
Stirrups
  #3 Ties
  14” o.c. (Maximum stirrup spacing)
Column 2

## Slide 14
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Initial Assumptions
9” Slab Thickness
  Based on 23’7” interior span
  Minimum thickness of ln/33
5,000 psi
No edge beams or drop panels
N

## Slide 15
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Slab Reinforcement
Top Cover: 1.5”
Bottom Cover: 1.5”
Design System: Two-Way Slab
N
▪ Latitude Design Strips for Floors 2 and 3

## Slide 16
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
N
▪ Locations of Punching Shear Failure

## Slide 17
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
N
▪ Locations of Punching Shear Failure

## Slide 18
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Punching Shear
Shear stress with unbalanced moment
  358.82psi
bo required due to this stress:
  bo=135”
Solution:
  28” by 28” by 12” deep shear caps
  Edge beams
67 k-ft

## Slide 19
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Final Slab
8” Thickness
  Meets deflection requirements
Bottom mat of #5 at 12” o.c. each way
Edge beams and shear caps where necessary
N
▪ Long Term Deflection on Second Floor

## Slide 20
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
▪ Reinforcement Plan of Second Floor
N
Column Strip
Middle Strip

## Slide 21
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Gravity System Redesign
Gravity Columns
Two-Way Flat Plate Slab
Transfer Beams
Transfer Beams
Existing Transfer Beam T1
  Width x Depth: 48” x 36”
  Bottom Bars: 14#10
  Top Bars: 8#9 at Full Length
  Stirrups: 4 Leg #4, 1 at 2” and rest at 8” on center
Existing Transfer Beam T2
  Width x Depth: 48” x 36”
  Bottom Bars: 12#9
  Top Bars: 6#9 at Full Length
  Stirrups: 4 Leg #4, 1 at 2” and rest at 12” on center
New Transfer Beam T1
  Width x Depth: 48” x 36”
  Bottom Bars: 14#10
  Top Bars: 12#10 at Full Length
  Stirrups: 4 Leg #4, 1 at 2” and rest at 6” on center
New Transfer Beam T2
  Width x Depth: 48” x 36”
  Bottom Bars: 12#9
  Top Bars: 8#9 at Full Length
  Stirrups: 4 Leg #4, 1 at 2” and rest at 12” on center

## Slide 22
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
Lateral Loads
Moment Frame Columns
Moment Frame Beams

## Slide 23
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
Moment Frames are located on exterior of structure to reduce twist
Difference between C.O.R. and C.O.M.
  For first 3 stories
    ~3 ft in X direction
    ~1 ft in Y direction
  For Fifth and Roof
    ~3 ft in X direction
    ~1.5 ft in Y direction
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams
COM
COR

## Slide 24
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams
Lateral Loads
Seismic was controlling case in both directions

## Slide 25
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams
Frames 1 and 2
Final Reinforcing
  2 Layers of 3#8
  #4 Stirrups spaced at 16” on center
Chart: Interaction Diagram for Frames 1 & 2
| 0 | 397.81915860835676 | 460.75788899957109 | 477.49856789176818 | 396.06201014638089 | 0
Capacity | 1232.5658 | 440.5656 | 396.202 | 379.7553 | 240.8041 | -255.96
Applied Load | 89.428
φPn(max) | 986.0526 | 986.0526

## Slide 26
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams
Frames 3 and 4
Final Reinforcing
  2 Layers of 4#8
  #4 Stirrups spaced at 16” on center
Chart: Interaction Diagram for Frames 3 & 4
| 0 | 444.20527178544017 | 519.85814460361803 | 540.83039390152419 | 452.89257721481937 | 0
Capacity | 1289.821 | 438.3833 | 393.4215 | 375.5866 | 228.3049 | -341.28
Applied Load | 175.2994
φPn(max) | 1031.8568 | 1031.8568

## Slide 27
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams
Frames 1 and 2
Final Reinforcing
  Bottom Bars: (4) #6 Full Length
  Top Bars: (3) #6 Full Length
  Stirrups: 2 leg #4 at 10” o.c.

## Slide 28
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams
Frames 3 and 4
Final Reinforcing
  Bottom Bars: (6) #6 Full Length
  Top Bars: (4) #8 Full Length
  Stirrups: 2 leg #4 at 10” o.c.

## Slide 29
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Lateral System Redesign
▪ Location of Moment Frames on Typical Plan
N
Lateral Loads
Moment Frame Columns
Moment Frame Beams

## Slide 30
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Construction Management Breadth
Breadth Topics:
      Impact on:
        Structural cost
        Critical Path
    Other Breadth Topics:
      Acoustical Consideration
        Impact on:
          STC Rating
          IIC Rating
Cost Analysis
Schedule Analysis

## Slide 31
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Construction Management Breadth
Cost Analysis
Schedule Analysis
Cost Analysis
The cost estimate for the redesign structure will take into account the following:
• Material costs of concrete mix for the slab, beams, columns, and shear caps
• Labor and equipment costs for placing the concrete mix with pumping
• Material and labor costs for formwork
• Material and labor costs for reinforcement of slabs and columns.
Individual Costs:
Concrete Mix: $272,200
Placing Concrete: $60,600
Formwork: $648,200
Rebar: $36,900
Total Cost: $1,063,500 or $212,700 per floor
Existing Structure Cost: $175,000 per floor
22% Increase in Cost

## Slide 32
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Construction Management Breadth
Cost Analysis
Schedule Analysis
Schedule Analysis
Existing schedule had a duration of 45 days for wood framing
Total duration of concrete structure was 69 days
  Increase of 24 days along the critical path
Placing of concrete and columns split into 3 zones
The duration for slabs and columns:
  Formwork: 2 days
  Reinforcement: 2 days
  Pour: 1 days

## Slide 33
Introduction ◆ Problem Statement/Goal ◆ Gravity System Redesign ◆ Lateral System Redesign ◆ Construction Management Breadth ◆ Conclusion/Acknowledgements
Thank you to the following people:
• Rathgeber and Goss Associates, especially Justin Domire
• AHC, Inc.
• Harkins Builders, especially Russell Tipton
• My classmates at Penn State along with my friends and family at home.
• Professors in the AE Department, especially my advisor Dr. Linda Hanagan.
Questions?

## Slide 34
Gravity Column Loads

## Slide 35
Gravity Column Loads

## Slide 36
Lateral Column Loads

## Slide 37
Lateral Beam Loads

## Slide 38
Lateral Beam Loads

## Slide 39
2nd Floor

## Slide 40
4th Floor

## Slide 41
5th Floor

## Slide 42
Roof

## Slide 43
2nd Floor

## Slide 44
4th Floor

## Slide 45
5th Floor

## Slide 46
Roof