## Slide 1
Brian J. Nahas [Construction Management Option]
Advisor: Dr. Robert Leicht
New Regional Medical Center
East Norriton, PA

## Slide 2
Brian J. Nahas [Construction Management Option]
Advisor: Dr. Robert Leicht
New Regional Medical Center
East Norriton, PA
implement virtual design and construction processes to identify options & trends in design, construction, and facility management

## Slide 3
New Regional Medical Center
East Norriton, PA
Project Background
Design
  Atrium Curtain Wall
  Pour Strip System
Preconstruction
  3D Quantity Takeoff & Estimating
Construction
  Steel Trending
  Crane Logistics
Turnover
  Industry Research
  FM Dashboard
  FM Interact
Recommendations

## Slide 4
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Owner’s Goals
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Project Background
“From its soaring atrium to its advanced imaging services, the center's architectural elegance is matched by top tier patient care capabilities.” Barry Freedman, President & CEO
Project Team Members
service to the community
hosting excellence in clinical care
fulfill the void in healthcare in Montgomery County
Location
East Norriton, PA
84-acre former golf course
access to major highways and state roads
Norristown Farm Park
Goal to preserve 1/3 of the campus as green space
Hospital Campus
Center City Philadelphia

## Slide 5
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Building Program
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Project Background
146 beds
  medical/surgical
  intensive care
  neo-natal
emergency care
trauma center (pending)
LEED certification (pending)
Architecture
precast panels
glazing units
curtain wall glazing
metal panel
Split-faced masonry block
Systems & Engineering
cast-in-place spread footings & foundation walls
structural steel system [30’ x 30’ grid]
  W12 & W14 columns| 1st & 3rd floor splices
  composite decking
composite curtain wall façade

## Slide 6
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Project Background
Construction Program & Logistics
$147 million | CM at Risk contract
Construction Schedule: July 6, 2010 – August 31, 2012
Staff Training: August 8 – October 15, 2012
Opening Day: September 29, 2012

## Slide 7
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Architectural Breadth Analysis
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
improve curtain wall constructability
addition of public space
modularization of glazing panels
Design
System | Cost
Floor System | $8,450
Structural Steel | $24,338
GWB | $3,280
Finishes | $87,387
Redesign Total | $123,455

## Slide 8
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Structural Breadth Analysis
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Design
Pour Strip Assembly* | 
Foundation System | $59,512
Structural Columns | $61,217
Structural Beams | $101,826
Slab on Grade | $684
Slab on Metal Deck | $9,230
Reinforcing | $7,303
Total: | $239,772
Existing System:
2 pour stops per floor
125 foot offset from east & west end wall
requires building enclosure & temperature regulation
*quantities derived through Revit design alternates
It is understood that this design decision may create construction issues, and areas for delay. Although this decision does not simplify the AEC’s project approach, it eases the maintenance and lifecycle control of the space… Focus on cost savings.
Richard Montalbano, Project Manager, Einstein Healthcare Network

## Slide 9
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Design
Expansion Joint Assembly |  | Diff.
Foundation System | $32,758 | -45%
Structural Columns | $60,671 | -1%
Structural Beams | $101,826 | -
Slab on Grade | $684 | -
Slab on Metal Deck | $8,552 | +7%
Reinforcing | $8,613 | +18%
Expansion Joint Covers | $40,289 | +100%
Misc. Steel Angle | $44,177 | +100%
Total: | $297,570 | +24%
Structural Breadth Analysis
Method:
calculate design tolerance & joint gap
size structural steel members
  tributary area
  load calculation
  locate splices
  design member per AISC Table 4-1
size spread footings per column case
model redesign
export quantities for estimate
Outcome:
2 expansion joints per floor
2” structural gap
use W12 x 50 & W12 x 40
13’ x 13’ x 30”
  #7 bars each way 6” oc
13.5’ x 13.5’ x 30”
  #7 bars each way 6” oc

## Slide 10
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
3D Quantity Takeoff
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Preconstruction
Model Estimating
Method:
create schedule of materials
export to excel
reference cost database
include non-modeled elements
produce estimate
Outcome:
CIP Concrete: +10.7% from as-built costs
Structural Steel: +0.5% from as-built costs
7.5% improvement on Gilbane’s method
Chart: 
| [2009] Interior Partition | [2010] Curtain Wall | [2012] CIP Concrete | [2012] Structural Steel
Time Savings | 0.2 | 0.89 | 0.8 | 0.8
Estimate Accuracy | 0.985 | 0.76 | 0.893 | 0.995

## Slide 11
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Steel Trending
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Construction
At each exchange point a thorough understanding is needed of who is involved, what software is involved, and what data needs to be exchanged (or can be exchanged) and what the data will be used for.”
Luke Faulkner, AISC Director of Information Technology Initiatives

## Slide 12
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Steel Trending
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Revit data to Excel Pivot Table & Chart
Chart: Critical Pick Workflow Trending By Elevation
| Sector A | Sector B | Sector C | Sector D | Sector D | Sector A | Sector B | Sector C | Sector D | Sector A | Sector B | Sector C | Sector D | Sector A | Sector A | Sector B | Sector A | Sector B | Sector A | Sector B | Sector A | Sector B | Sector A | Sector B | Sector A | Sector B | Sector A | Sector A | Sector A | Sector B | 00'-0" | 04'-0' | 14'-8" | 29'-4" | 31'-4" | 36'-8" | 44'-0" | 51'-1" | 58'-8" | 70'-10" | 73'-4" | 77'-0" | 90'-0 3/8" | 91'-2"
Total | 0.42123 | 1.7233 | 0.11021 | 1.0962 | 1.056 | 17.532 | 2.2437 | 2.5208 | 1.316 | 10.872 | 2.9845 | 2.303 | 2.285 | 3.502 | 0.50292 | 7.2911 | 8.316 | 2.8575 | 3.502 | 0.5145 | 17.532 | 2.8575 | 3.5644 | 0.48387 | 11.4367 | 3.0887 | 3.7852 | 3.502 | 5.395 | 0.18016
Construction
Column Splice [Lift 1]
Column Splice [Lift 2]
Column Splice [Lift 3]

## Slide 13
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Steel Trending
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Construction
Chart: Critical Pick Workflow Trending By Sector
| 00'-0" | 14'-8" | 29'-4" | 31'-4" | 36'-8" | 44'-0" | 51'-1" | 58'-8" | 70'-10" | 73'-4" | 77'-0" | 90'-0 3/8" | 91'-2" | 00'-0" | 14'-8" | 29'-4" | 36'-8" | 44'-0" | 51'-1" | 58'-8" | 70'-10" | 73'-4" | 91'-2" | 00'-0" | 14'-8" | 29'-4" | 00'-0" | 04'-0' | 14'-8" | 29'-4" | Sector A | Sector B | Sector C | Sector D
Total | 0.42123 | 17.532 | 10.872 | 3.502 | 0.50292 | 8.316 | 3.502 | 17.532 | 3.5644 | 11.4367 | 3.7852 | 3.502 | 5.395 | 1.7233 | 2.2437 | 2.9845 | 7.2911 | 2.8575 | 0.5145 | 2.8575 | 0.48387 | 3.0887 | 0.18016 | 0.11021 | 2.5208 | 2.303 | 1.0962 | 1.056 | 1.316 | 2.285
Revit data to Excel Pivot Table & Chart

## Slide 14
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Crane Logistics
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
300 Ton Lattice Crane
Mobilization & Demobilization Costs: $9,000 x 2 = $18,000
Rental Costs: $20,000 x 18 weeks = $360,000
TOTAL: $378,000
300 Ton Lattice Crane & 110 Ton Mobile Crane
Mobilization & Demobilization Costs: $9,000 x 2 + $3,400 x 2 = $24,800
Rental Costs: $20,000 x 15 weeks + $5,840 x 3 weeks = $317,520
TOTAL: $342,320
Results:
2 week schedule reduction: $280,047 [general conditions]
Crane rental: $35,680
Total Project Savings: $315,727
Construction
110 Ton Mobile Crane
300 Ton
Lattice Crane

## Slide 15
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Industry Research
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Turnover
Chart: 
| Architect | Architect/Engineer | Contractor/Engineer | Engineer | Engineer/Architect | General Contractor/CM Firm | Technology Consultant | Software Developer/Vendor | Hardware Developer/Vendor | Academic Research | Specialty/Subcontractor
Respondent Type (%) | 10.6 | 10.9 | 22.1 | 25.3 | 8.6 | 32.2 | 5.2 | 6 | 2 | 2.6 | 9.8
01 ¦ BIM | 02 ¦ iPads | 03 ¦ Collaboration Environment
04 ¦ Online Project Documents | 05 ¦ 3D CAD | 06 ¦ Mobile Tools & Devices
01 ¦ Cheaper, Better Software | 02 ¦ Data Integrations (BIM) | 03 ¦ Online Collaboration
04 ¦ Mobile Hardware | 05 ¦ Cloud Storage & Tools | 06 ¦ Linked & Live Project Controls
Current Information Technology Use
Desired Information Technology
Owner Interview
Current Use
  Paper Plan Room
  Outdated As-Built information
Desired Use
  Room Data Log
  As-Built Drawings
  Submittal Log
“The words that came up most often were ‘cheaper,’ ‘simpler,’ streamlined,’ ‘user-friendly,’ ‘interoperable,’ and ‘integrated’.”
Tom Sawyer, Engineering News-Record

## Slide 16
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Turnover
FM Dashboard
  Room Log
  Direct access to equipment files
  Construction & As-built Photographs
  As-Built Drawings
  PDF Digital Set
  Hyperlinked details
  Submittal / O&M
  Material Submittal Information
  Equipment & Room Locations
“A FM document interface should not consist of a series of internet pages built around a specific Attribute; it should consist of an interface which reads a database of relative information, data, and asset.”
Dr. Craig Dubler, Office of the Physical Plant [PSU]

## Slide 17
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Turnover
FM Interact
Microsoft Silverlight – Pivot Viewer
Filter Parameter | Document Data & Relationships
System | Construction Photos, Submittals, RFI’s, Contract Drawings, Design Model, As-Built Model, Equip. Data Sheet
Zoom Format | JPG, TIFF
Link to Original File | JPG, PDF, RVT, DWG, NWD, DOC, XLS, SKP, Hyperlink, Other
Document Name | Individual Description
Campus | East Norriton
Facility Name | New Regional Medical Center
Building Sector | A, B, C, D, Central Utility, Site
Floor Level | Ground Level, 1, 2, 3, 4, Roof
Room Number | ####
Date Added to Database | YYYY-MM-DD
Model/Drawing | Yes, No
CSI Discipline | ## - Title
Bid Package # | BP ##
Trade Contractor | Company Name
Trade Contact | Contact – linked to email address
Design Team | Company Name
Design Contact | Contact – linked to email address
Construction Manager | Company Name
Construction Contact | Contact – linked to email address
Asset Management | Hyperlink to external software/file

## Slide 18
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Design
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Recommendations
Atrium & Pour Strip Redesign
Benefit to NRMC: NO
Benefit to the Industry: YES
Development: Externally
Preconstruction
3D Quantity Takeoff & Estimate
Benefit to NRMC: YES
Benefit to the Industry: YES
Development: Internally
Construction
Steel Trending
Benefit to NRMC: YES
Benefit to the Industry: YES
Development: Internally
Turnover
Document Management
Benefit to NRMC: YES
Benefit to the Industry: YES
Development: Internally & Externally

## Slide 19
Presentation Outline
Project Background
VDC Implementation
  Design
    Atrium Curtain Wall
    Pour Strip System
  Preconstruction
    3D QTO & Estimating
  Construction
    Steel Trending
    Crane Logistics
  Turnover
    FM Documentation
    FM Interact
Recommendations
Acknowledgements
Industry Acknowledgements
Brian J. Nahas [Construction Management Option]
New Regional Medical Center
East Norriton, PA
Acknowledgements
Richard Montalbano & the Facility Management Staff at Albert Einstein Healthcare Network
Andrew Packer & Jerry Shaheen at Gilbane Building Company
Gene Hodge, Jason Brown, Nicholas Kantor, & Michal Wojtak at Mortenson Construction
Dr. Craig Dubler & the Facility Management Staff at Penn State’s Office of Physical Plant
PACE Industry Members
My Family & Friends
Special Thanks
VDC implementation goes beyond the utilization of models and design software.
Additional insight into design data produces a stronger understanding of construction and FM usage.
Lessons Learned

## Slide 20
Brian J. Nahas [Construction Management Option]
Advisor: Dr. Robert Leicht
New Regional Medical Center
East Norriton, PA
implement virtual design and construction processes to identify options & trends in design, construction, and facility management