## Slide 1: Frederick College of Cardiology Arlington Heights, IL
Schematic Design Presentation
by Rob Currie

## Slide 2: Building Usage
Education facility for Physicians and Physicians in training
Auditorium for conferences and demonstrations
Office space for administration employees
Similar to the IALD of Cardiologists

## Slide 3
Auditorium
48,000 sq. ft.

## Slide 4: The Manikin

## Slide 5: The Human Body

## Slide 6: Deconstructed
Unfamiliar Out of Context

## Slide 7: Deconstructed
Unfamiliar Out of Context

## Slide 8: Deconstructed
Unfamiliar Out of Context

## Slide 9: Studying the Unfamiliar
Lighting in Unexpected Ways

## Slide 10: Focus Spaces
Auditorium
Open Office
  Psychological Impression
Main Lobby
  3 Schematic Design Concepts
Façade

## Slide 11: Auditorium> Floor Plan
Auditorium

## Slide 12: Auditorium> Floor Plan

## Slide 13: Auditorium> Design Criteria + Considerations
SETTING | Illuminance Horiz. | Height | Illuminance vert. | Height | Uniformity
Lecture Setting A/V with notes | 50 lux | @ 2’ a.f.f. | 15lux | @ 4’ a.f.f. | 2:1 Avg:Min
Lecture Setting A/V without notes | 10 lux | @ floor | 6lux | @ 4’ a.f.f. | 2:1 Avg:Min
Lecture Setting no A/V | 100 lux | @ 2’ a.f.f. | 40lux | @ 4’ a.f.f. | 2:1 Avg:Min
Demonstration | 1000 lux | @ 3’ a.f.f. | 500lux | @ 4’ 6” a.f.f. | 3:1 Avg:Min
Concentrated light levels specifically for lighting surgical demonstrations in the front of the auditorium will be necessary. Spot lighting should create high illuminance on the demonstration area while not causing additional glare on the projector screen.
Control system must be able to control the auditorium in full mode and in separate sections.
- Lighting controls must be useful for many different activities in the space but also simple for use by educators and students. (IES The Lighting Handbook, pg. 24.3)

## Slide 14: Auditorium> Schematic Design > Sketches

## Slide 15: Auditorium> Schematic Design > Sketches

## Slide 16: Auditorium> Schematic Design > Sketches

## Slide 17: Auditorium> Schematic Design > Sketches

## Slide 18: Auditorium> Schematic Design > Sketches

## Slide 19: Auditorium> Psychological Impression > Spacious
Ambient lighting creates uniformity
Walls and ceiling highlighted
Deconstructed ceiling creates the illusion of a extended space beyond the actual ceiling

## Slide 20: Auditorium> Schematic Design > Sketches
Deconstructed ceiling blurs the lines between regular surfaces of the space.
Illumination originates from a hidden source
Gaps in ceiling suggest that there is a larger unkown space behind the plane of the ceiling.

## Slide 21: Auditorium> Schematic Design > Controls

## Slide 22: Auditorium> Schematic Design > Controls
Controls system must adapt to address both auditorium spaces as one unit or two separate rooms.
“Sky Fold” wall triggers control system mode of operation.
Wall is up > Controls merge both rooms fixtures together
Wall is down > Controls separate both spaces fixtures
Bright illuminance at front of room for demonstrations must be controlled as to not wash out projector screens operating in close proximity

## Slide 23: Open Office > Floor Plan
Office

## Slide 24: Open Office > Design Criteria & Considerations
SETTING | Illuminance Horiz. | Height | Illuminance vert. | Height
VDT Screen and keyboard + polarity | 300lux | @ 2’ 6” a.f.f. | 150lux | @ 4’ a.f.f.
VDT Screen and keyboard - polarity | 150lux | @ 2’ 6” a.f.f. | 50lux | @ 4’ a.f.f.
Reading 12 point font | 200lux | @ 2’ 6” a.f.f. | 50lux | @ 5’ a.f.f.
Visual rest from typical tasks of reading and writing should be provided
Day lighting and views should be incorporated into a successful design
Day lighting automated shades and dimming control implemented
- Direct glare from luminaires should be avoided

## Slide 25: Open Office > Schematic Design
Office

## Slide 26: Open Office > Schematic Design
Office

## Slide 27: Open Office > Schematic Design
Office
Micro-Prismatic Lens
LED Task Lighting

## Slide 28: Open Office > Daylighting
Office
Full window exposure on East and West sides of the office wing

## Slide 29: Main Lobby > Floor Plan
Lobby

## Slide 30: Main Lobby > Floor Plan

## Slide 31: Main Lobby > Design Criteria & Considerations
SETTING | Illuminance Horiz. | Height | Illuminance vert. | Height | Uniformity
Lobby @ building entrance DAY | 100lux | @ floor | 30lux | @ 5’ a.f.f. | 4:1 Avg:Min
Lobby @ building entrance NIGHT | 50lux | @ floor | 20lux | @ 5’ a.f.f. | 4:1 Avg:Min
Lobby distant from entries | 100lux | @ 2’ a.f.f. | 30lux | @ 5’ a.f.f. | 4:1 Avg:Min
Lobby desk top | 150 | @3 6” a.f.f. | N/A | N/A | 4:1 Avg:Min
Day lighting should be used as a large component of lighting the space during daytime hours.
Transitional brightness at entrances should be considered to aid adaptation.
Lobby should exemplify the character of the occupant through referencing the work of the college in the lighting design.
Wayfinidng emphasis building spaces

## Slide 32: Main Lobby > Schematic Design 1

## Slide 33: Main Lobby > Schematic Design 1

## Slide 34: Main Lobby > Schematic Design 1

## Slide 35: Main Lobby > Schematic Design 1

## Slide 36: Main Lobby > Schematic Design 1

## Slide 37: Main Lobby > Schematic Design 1

## Slide 38: Main Lobby > Schematic Design 1

## Slide 39: Main Lobby > Schematic Design 1

## Slide 40: Main Lobby > Schematic Design 1
Light Spots create points of discontinuity in the planes of the space.
The pattern of spots continues from floor to wall and connects horizontal and parallel surfaces.
Transitional brightness at entrances will aid adaptation in daylight scenarios.
Light spots aid in way finding and highlight important locations in the Lobby

## Slide 41: Main Lobby > Schematic Design 2

## Slide 42: Main Lobby > Schematic Design 2

## Slide 43: Main Lobby > Schematic Design 2

## Slide 44: Main Lobby > Schematic Design 2

## Slide 45: Main Lobby > Schematic Design 2

## Slide 46: Main Lobby > Schematic Design 2

## Slide 47: Main Lobby > Schematic Design 2

## Slide 48: Main Lobby > Schematic Design 2

## Slide 49: Main Lobby > Schematic Design 2
Linear LED rgb fixture

## Slide 50: Main Lobby > Schematic Design 2
Why Color?
Colored ambient lighting creates unfamiliar atmosphere
Colored wall bright enough to illuminate faces and features of people in waiting area.
Color will render faces and features in new ways and will be ever changing.
Water feature lighting will reinforce color as a theme in the space
Lobby desk will also highlight color on the front fascia.

## Slide 51: Main Lobby > Schematic Design 3

## Slide 52: Main Lobby > Schematic Design 3

## Slide 53: Main Lobby > Schematic Design 3

## Slide 54: Main Lobby > Schematic Design 3
Microscope slide creates intricate organic patterns
Similar system would project biological pattern into space
Pattern will cover parts of the ground and some walls

## Slide 55: Facade> Design Criteria + Considerations
Due to the semi-commercial residential nature of the surrounding areas I believe the college should be categorized as LZ2, medium activity.
SETTING | Illuminance vert. | Uniformity
Lighter toned façade material | 20lux | 3:1
Darker toned façade materials | 40lux | 3:1
Determine lowest acceptable light level
Control light levels to operate between dusk and curfew hours
Select luminaires for specific optical control to reduce glare

## Slide 56: Facade> Schematic Design

## Slide 57: Facade> Schematic Design

## Slide 58: Facade> Schematic Design
Highlights continuous surface which exists in multiple planes

## Slide 59: Facade> Schematic Design

## Slide 60: Facade> Schematic Design

## Slide 61: Facade> Schematic Design

## Slide 62: Facade> Schematic Design > Fixtures
Exterior Linear LED
Mounted to upper edge of surrounding facia

## Slide 63: THE END