Timothy R. Nolan

Mechanical

Consultant Unknown

The Bond Street Wharf

Baltimore, Maryland

September 12, 2002

Overall Existing Conditions Summary

Executive Summary:

The Bond Street Wharf is a six story multi-use building located in Baltimore, Maryland.  It took a year and four months to build and costs $21 million.  RTKL, an architectural engineering firm, designed the major components of the building while Struever Bros. Eccles & Rouse, the main contractor, oversaw the construction.  The structure is reinforced concrete with a red brick facade. The red brick matches the existing buildings surrounding the area.  It is a state of the art building with an under floor air distribution system and multi dimensional telecommunication structure.  It is well-located near the highway and public transportation for easy access.

Timothy R. Nolan

Mechanical

Consultant Unknown

The Bond Street Wharf

Baltimore, Maryland

September 12, 2002

Primary Project Team:

- Owner: 				Bond Street Wharf, LLC.

- Architects: 				RTKL Associates Inc.

One South Street

Baltimore, MD 21202

- Structural Engineers:  		RTKL Associates Inc.

- MEP and Telecom Engineers:	RTKL Associates Inc.

- Civil Engineers:			STV Inc.

21 Governor’s Court

Baltimore, MD 21244

- General Contractor:			Struever Bros. Eccles & Rouse, Inc

1040 Hull Street Suite 200

Baltimore, MD 21230

- Graphic Designers:			ID8, RTKL Associates Inc.

- Landscape Architects:		Mahan Rykiel Associates Inc.

1330 Smith Avenue

Baltimore, MD 21209

- Code Consultants:			Hughes Associates, Inc.

3610 Commerce Drive, Suite 817

Baltimore, MD 21227

Timothy R. Nolan

Mechanical

Consultant Unknown

The Bond Street Wharf

Baltimore, Maryland

September 12, 2002

Dates of Construction:

- Start:  June 2001

- Finish:  October 2002

Cost Information:

- Total cost was $21 million.

- Mechanical cost was $3,250,000.

Building Function and Use:

- Multi-use office building with retail.

- Function over Form.

Location and Site:

- 901 South Bond Street, Baltimore, Maryland.

- Located in Fells Point near downtown.

Architecture:

- Typical red brick to match the surrounding Fells Point buildings.

- Six stories tall with approximately 36,000 square feet per floor.

- 12,300 square feet of retail space.

- Water front promenade and a terrace on the roof.

Major National Model Codes:

- BOCA Nation Building Code(1996 Edition)

- The Baltimore City Code (1997 Edition)

- BOCA National Fire Prevention Code (1996 Edition)

- The Baltimore City Fire Prevention Code (1997 Edition)

- ASME (1993 Edition)

Timothy R. Nolan

Mechanical

Consultant Unknown

The Bond Street Wharf

Baltimore, Maryland

September 12, 2002

Zoning and Historical:

- Zoned for commercial and offices.

Project Delivery Method:

- Design, Bid, Build.

Building Envelope:

Wall:

- Concrete masonry units with red face brick

- 1/16” Asphaltic Compound for Damp-proofing.

- Extruded Polystyrene Board Insulation with an R value of 13.

- Cast stone with wooden accents.

Windows:

- Double Glazed, 1” thick ( ¼”clear glass, ½” dehydrated airspace, ¼” clear glass), low E.

Roof:

- Galvanized Steel deck with R-19 insulation and protection board.

- Fluoropolymer waterproof coating.

- 24”x 24”, 2” thick Concrete Pavers on pedestals for drainage.

Structural:

- Reinforced concrete structure with 10 foot high ceilings.

- The south half of this building is sitting on an eroding pier.  They poured a structural slab for the first floor south instead of slab on grade.  They took the piers down to over 95 feet below grade for support.

Timothy R. Nolan

Mechanical

Consultant Unknown

The Bond Street Wharf

Baltimore, Maryland

September 12, 2002

Electrical:

Panel Boards:

- 7- 277/480, 3 phase, 4 wire, 300 Bus Amps

- 14- 277/480, 3 phase, 4 wire, 100 Bus Amps

- 14- 120/208, 3 phase, 4 wire, 100 Bus Amps

Switchboard:

- 277/480, 3 phase, 4 wire, 800Amps

- 277/480, 3 phase, 4 wire, 3000Amps

- 277/480, 3 phase, 4 wire, 2000Amps

Generator:

- 375 KVA, 300 KW, Fuel oil

Lighting:

Interior:

- 6” Recessed Ceiling Mounted Down-lighting in corridors and lobby areas on floors 2-6.

- 2’ x 4’ Recessed ceiling mounted fluorescent light in open office spaces.

Exterior:

- Surface mounted lighting to accent structure features.

- Surface wall mounted to accent doors and windows

Fire Protection:

- Passive and Active.

- Automatic sprinkler system with heat responsive element and ½” orifice.

- Ductile and Schedule 10, 30, 40 steel pipe system.

- Smoke detector for HVAC, stairways and elevators lobbies.

- Heat detectors in elevator machine rooms.

- 1 to 2 hour fire rated construction.

Timothy R. Nolan

Mechanical

Consultant Unknown

The Bond Street Wharf

Baltimore, Maryland

September 12, 2002

Mechanical:

- State of the art Air Handling Units, with individual tenant climate controls.

- Raised floor air distribution system that improves indoor air quality and employee comfort.

- 3 Cooling towers with a total capacity of 1016 tons.

- 11 Air Handling Units with a total of 256,000 CFM.  Each floor has two AHU, excluding the 1st floor.

- 1 Boiler with a capacity of 245 MBH

- 3 Heat Exchangers with 2900 GPM total capacity

- 2-12,000 CFM Outdoor AHU

- 9 Pumps with 10,900 GPM capacity

Transportation:

- 2 Stairways.

- 4 Electric Elevators to reach any floor under 6 seconds.

Telecommunication:

- Capacity for various data and communications links.

- Secure card access system.

Special Systems:

- Convenient access to highways, water taxi and public transportation.