## Slide 1
Daniel Suter
Construction Management
AE Senior Thesis Presentation
The Pennsylvania State University
Unknown Data Center
Somewhere, USA
4.12.2011

## Slide 2
2
Daniel Suter | Construction Management | 4.12.2011
Unknown Data Center
Somewhere, USA
Agenda
Project Overview
Analysis One: Alternate Roof Systems
  Electrical Breadth
Analysis Two: Façade Redesign
  Structural Breadth
Analysis Three: Tablet PC’s
Conclusions
Questions

## Slide 3
Agenda
PROJECT OVERVIEW
Project Overview
Analysis One: Alternate Roof Systems
  Electrical Breadth
Analysis Two: Façade Redesign
  Structural Breadth
Analysis Three: Tablet PC’s
Conclusions
Questions
  Owner
    Anonymous
  Occupancy Type
    Business
  Size
    17,445 SF
  Cost
    $ 50 Million (Design+Construction)
  Construction Duration
    December 2008 – August 2010
  Delivery Method
    Design-Bid-Build
3
Daniel Suter | Construction Management | 4.12.2011
Unknown Data Center
Somewhere, USA

## Slide 4
Agenda
Project Overview
Analysis One: Alternate Roof Systems
  Electrical Breadth
Analysis Two: Façade Redesign
  Structural Breadth
Analysis Three: Tablet PC’s
Conclusions
Questions
Daniel Suter | Construction Management | 4.12.2011
Unknown Data Center
Somewhere, USA
ANALYSIS ONE – Alternate Roof System
  Opportunity
  The Data Center’s roof construction primarily constructed with EPDM fully adhered to concrete slab on deck. On top of the EPDM is interlocking insulation board covered with UV protection fabric and is topped off with interlocking concrete pavers. This type of roof was selected for sound isolation purposes. The primary problem is that the owner is not utilizing the opportunity to implement green/solar roofing systems to increase to performance of his/hers building. In addition, the current roof constructed includes various amounts of materials and two different trades to construct this roof type.
  Objective
  The expected outcomes from this analysis will conclude that a PV panel roofing system will be more beneficial to the owner because of the type of building it is. The effects on duration and cost will be affected in a negative way, but the life cost cycle will make up for the longer duration and cost to the owner
4

## Slide 5
Agenda
Project Overview
Analysis One: Alternate Roof Systems
  Electrical Breadth
Analysis Two: Façade Redesign
  Structural Breadth
Analysis Three: Tablet PC’s
Conclusions
Questions
Daniel Suter | Construction Management | 4.12.2011
Unknown Data Center
Somewhere, USA
Structural Breadth
  Overview:
  In attempt to redesign the current architectural precast panels. This analysis will include redesigning the 20 foot parapet walls, while collaborating with the architect. Different size beams and columns may arise through the structural calculations that will be performed.
5
3D Model Insert