## Slide 1
The Sunshine Elementary School
Redesign Proposal
Pennsylvania State University
AE Senior Thesis
Nicholas Scheib
Mechanical Option- IP

## Slide 2
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
The Sunshine Elementary School is located in Climate Zone 5. The design has met all ASHRAE requirements of this climate zone.
ASHRAE Climate Chart (Fundamentals, 2009)
General Information of Project
Size- 103,000 Square Feet
2 Levels
Overall Cost- $16,599,000
Brick Facade
Gable Roofs
Construction Dates- March 2010- June 2011
Silver LEED Accreditation Goal

## Slide 3
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
Water-to-Air Heat Pumps Tied to Ground Loop
Original Design Components
144 Vertical Geothermal Wells- 12 x 12 grid
Water-to-Air Heat Pumps- each room
Energy Recovery Units
CO2 Sensors
AHU’s for gym and cafeteria
eQuest© Energy Model- LEED approved
  42% more efficient then Baseline Model

## Slide 4
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
Radiant Heating and Cooling
Enough Capacity?
Radiant heating and cooling was designed in the gymnasium, 1st through 5th grade classrooms and kindergarten classrooms.

## Slide 5
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
Using coefficients found by Bjarne W. Olesen the Radiant heating and Cooling capacities were found.
The cooling Capacity of a radiant slab is less then that of heating.
Radiant Capacity = Coefficient* Floor Area * ∆T

## Slide 6
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
Conditioning Ventilation air will increase the system capacity but will prove to still not be enough.
Radiant Capacity + (1.08 x CFM x ∆T) = Total Capacity
By adding daylighting controls to the building the peak cooling demand is now met.

## Slide 7
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros Versus Cons
Low Velocity Displacement Ventilation couples well with radiant systems by increasing the stratification of the space.
The combined effect of radiant systems and low velocity displacement ventilation treats the load where the demand is located.
(Price, 2007)
(Price, 2007)

## Slide 8
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
The Air Change Effectiveness (Ez) is increased to 1.2 allowing of 30% increased outdoor air while reducing CFM by 13%.
Increased Outdoor Air and contaminant controls greatly improves the indoor environment.
(Price, 2007)

## Slide 9
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
Additional benefits are added by reducing needed ductwork to typical classrooms.
Original Ductwork
Redesign Ductwork
Without the need for ductwork above the suspended ceiling building height can be lowered by 32”.

## Slide 10
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
IESNA Lighting Design Guide the task of using a #2 pencil and softer leads is a performance of high contrast and large size.
Typical 1st Classroom South Sept. 21 at 12pm
Typical 2nd Classroom South Sept. 21 at 12pm
The North facing classrooms receive less daylight then the South facing classrooms but still have dimming potential.
Typical 1st Classroom North Sept. 21 at 12pm
Typical 2ndClassroom North Sept. 21 at 12pm

## Slide 11
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
The redesign of the ventilation system changed the noise criteria rating of the air supply to the classrooms.
The noise criteria is reduced from a NC-39 to a NC-19 due to more attenuation within the duct work.

## Slide 12
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
Using RS Means a cost comparison was calculated for all changes made to original design.
Overall the redesign was a 5% increase when compared to the initial cost.

## Slide 13
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  Life-Cycle Cost Analysis
Pros versus Cons
Annual Energy Savings of the proposed redesign compared to the original design were calculated.
The savings in electric were then calculated using the electrical rates supplied by the designer.

## Slide 14
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  Life-Cycle Cost Analysis
Pros Versus Cons
The Analysis showed a payback period of 10.5 years for the changes to the original design.
A Life-Cycle Cost Analysis was performed for the annual energy savings versus initial cost.

## Slide 15
Presentation Outline
Project Overview
Existing Conditions
Depth
  Radiant Heating and Cooling
  Low Velocity Displacement Ventilation
Breadths
  Daylighting
  Acoustics
Overall Cost
  Initial Difference
  LCC
Pros versus Cons
The increase indoor environment is a major benefit of the proposed redesign.
The redesign is considered to be feasible and is recommended.
Questions?
Increased IAQ
Contaminant Control
Warm Floor for Kindergarten
Increased Thermal Comfort
6% Energy Reduction
Con’s
5% Increased Initial Cost
Increased Construction Time
30% Increased Ventilation
Decreased Mechanical Noise
225K Payback over 25yrs
Reduced Absences
Increased Test Scores
Pros