## Slide 1
James W. & Frances G. McGlothlin Medical Education Center
Virginia Commonwealth University School of Medicine
(VCU SOM)
Richmond, VA
Marissa Delozier
{Structural Option}
Faculty Consultant: Hanagan
Introduction

## Slide 2
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Building Statistics
VCU SOM
220, 000 GSF
13 stories above ground
Multipurpose (Admin, Classrooms, Labs)
$159 million
October 2009 to March 2013
Designed for LEED Silver Certification

## Slide 3
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Primary Project Team
VCU SOM
Notes: Owner – Virginia Commonwealth University
CM – Gilbane Building Company
Architect + Engineers – Ballinger
Exterior Architect – Pei Cobb Freed & Partners
Civil Engineer – Draper Aden Associates
Geotechnical Engineers – Geotech, Inc.

## Slide 4
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Existing Gravity System
VCU SOM
Drilled piers + caisson-grade beam system
N

## Slide 5
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Existing Gravity System
VCU SOM
Drilled piers + caisson-grade beam system
Composite Steel Flooring
3” 20 gauge decking
3 ½” LW concrete topping
Wide Flange Steel Beams + Girders
Typical Bay Sizes
30’ x 20’
30’ x 40’
N

## Slide 6
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Existing Lateral System
VCU SOM
Concentrically braced frames + moment connections
7 total, majority in one direction
Both wide flange + HSS
N

## Slide 7
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Opportunities
VCU SOM
Increase efficiency of structural system
Save both time + money
In line with VCU SOM reinvented curriculum, create open environments

## Slide 8
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Opportunities
VCU SOM
Increase efficiency of structural system
Save both time + money
In line with VCU SOM reinvented curriculum, create open environments
Proposal
Design alternate structural system
Non-composite deck + K-series joists + girders
Heavier emphasis on use of moment frames
Evaluate cost + schedule of redesign
Structural Costs vs. Total Project Costs
Investigate impacts on Architecture
Can a more open concept be achieved?
Can improvements be made?

## Slide 9
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Gravity System
VCU SOM
Possible Bay Configurations
30’ x 20’ – Joists traveling in 30’ direction
30’ x 40’ – Joists traveling in 30’ direction
30’ x 20’ – Joists traveling in 20’ direction
30’ x 40’ – Joists traveling in 40’ direction
30’
40’

## Slide 10
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Gravity System
VCU SOM
Possible Bay Configurations
30’ x 20’ – Joists traveling in 30’ direction
30’ x 40’ – Joists traveling in 30’ direction
30’ x 20’ – Joists traveling in 20’ direction
30’ x 40’ – Joists traveling in 40’ direction
Layout | Decking | Joists | Girders
I | 1.0C24 | 22K10 | W18x35
Hand Calculations
II | 1.0C24 | 22K10 | W24x146
III | 0.6C24 | 14K4 | W24x68
IV | 0.6C24 | 26K12 | W24x76

## Slide 11
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Gravity System
VCU SOM
Layout | Bay Size | Walking Evaluation < 0.5 % g | Floor Stiffness < 9 Hz | Final Evaluation
I | 30’x20’ | 0.47 % g | 5.47 Hz | Pass
II | 30’x40’ | 0.28 % g | 3.54 Hz | Pass
III | 30’x20’ | 0.38 % g | 4.77 Hz | Pass
30’
40’
IV | 30’x40’ | 0.58 % g | 3.93 Hz | Fail

## Slide 12
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Gravity System – Final Redesign
VCU SOM
Layout | Bay Size | Decking | Joists | Girders
I | 30’x20’ | 1.0C24 | 22K10 | W18x40
Layout | Bay Size | Decking | Joists | Girders
II | 30’x40’ | 1.0C24 | 22K10 | W30x124

## Slide 13
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Lateral System
VCU SOM
Existing Lateral System – Braced Frames
Proposed Lateral System – Moment
Braced
N

## Slide 14
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
RAM Model
VCU SOM
Center of Mass + Center of Rigidity
Center of Mass (88, 43.5)
Center of Rigidity (91, 39)

## Slide 15
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
RAM Model
VCU SOM
Center of Mass + Center of Rigidity
Drift Checks
Wind Loadings – Case 1 Controls
Seismic Loadings
Maximum Drifts
Loading | Drift | Allowable Drift
Wind – Case 1 | 0.42 | 0.44
Wind – Case 2 | 0.32 | 0.44
Wind – Case 3 | 0.32 | 0.44
Wind – Case 4 | 0.25 | 0.44
Seismic | 0.62 | 2.9

## Slide 16
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Frame Participation
VCU SOM
Frame # | 1 | 2 | 3 | 4 | 5 | 6
Avg. Load | 20% | 32% | 20% | 5% | 5% | 18%
Proposed Lateral System
1
2
3
6
4
5

## Slide 17
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Frame Participation
VCU SOM
Frame # | 1 | 2 | 3 | 4 | 5 | 6
Avg. Load | 20% | 32% | 20% | 5% | 5% | 18%
Frame # | 7 | 8 | 9 | 10
Avg. Load | 5% | 54% | 15% | 26%
Proposed Lateral System
1
2
3
6
4
5
7
8
9
10

## Slide 18
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Cost & Schedule Analysis
VCU SOM
{Breadth 1}

## Slide 19
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Cost & Schedule Analysis
VCU SOM
{Breadth 1}
Original System | 
Concrete | $ 1.16
Conc. Placing | $ 0.25
Conc. Finishing | $ 0.14
Shear Studs | $ 0.16
Beams | $ 4.20
Girders | $ 11.72
Decking | $ 2.80
Fireproofing | $ 0.81
Total ($/SF) | $ 21.23
Structural System Costs
Total Project Costs
Curtain Wall Changes
Additional Fireproofing
Schedule Comparison
Redesigned System | 
Concrete | $ 1.25
Conc. Placing | $ 0.18
Conc. Finishing | $ 0.67
K-Series Joists | $ 3.41
Girders | $ 8.17
Decking | $ 2.22
Fireproofing | $ 1.70
Total ($/SF) | $ 17.61

## Slide 20
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Cost & Schedule Analysis
VCU SOM
{Breadth 1}
Structural System Costs
Total Project Costs
Curtain Wall Changes
Additional Fireproofing
Schedule Comparison
System | Floor-to-Floor | Ceiling Ht | Total Height
Original | 14’ – 8” | 11’ – 0” | 196’ – 0”
Redesign Option 1 | 14’ – 8” | 10’ – 6” | 196’ – 0”
Redesign Option 2 | 15’ – 2” | 11’ – 0” | 202’ – 6”
Notes: Option 1 – Same Floor-to-Floor Height (vs Original)
Option 2 – Same Ceiling Height (vs Original)

## Slide 21
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Cost & Schedule Analysis
VCU SOM
{Breadth 1}
Structural System Costs
Total Project Costs
Curtain Wall Changes
Additional Fireproofing
Schedule Comparison
System | Original
Decking | Meets 2 HR
Steel | Spray
Ceiling | Non-Rated
Sprinkler | Yes
Price Increase | –
Redesign – B
Meets 2 HR
Factory Applied+Spray
Rated
No
$ 1.20/SF
Redesign – A
Meets 2 HR
Spray
Non-Rated
Yes
$ 0.92/SF

## Slide 22
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Cost & Schedule Analysis
VCU SOM
{Breadth 1}
Structural System Costs
Total Project Costs
Curtain Wall Changes
Additional Fireproofing
Schedule Comparison
Task | Original Duration | Redesign Duration
Steel Erecting + Detailing | 122 days | 114 days
Deck Pour/ Fireproofing | 89 days | 93 days

## Slide 23
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Architectural Impacts
VCU SOM
{Breadth 2}

## Slide 24
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Architectural Impacts
VCU SOM
{Breadth 2}
Creating an Open Environment
Fireproofing Redesign
Occupancies
Additional Fire Barriers
Removal of Sprinklers

## Slide 25
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Architectural Impacts
VCU SOM
{Breadth 2}
Creating an Open Environment
Fireproofing Redesign
Occupancies
Additional Fire Barriers
Removal of Sprinklers
Floor | Main Occupancies
1 – 3 | A & B
4 | B
5 – 8 | A & B
9 | B
10 | B
11 | A & B
12 | A & B
Additional Fireproofing
–
65 LF
300 LF
25 LF
65 LF
150 LF
55 LF
Sprinklers Removed
–
120
90
150
120
100
100

## Slide 26
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Conclusions
VCU SOM
Increase efficiency of structural system
Save both time + money
In line with VCU SOM reinvented curriculum, create open environments
Designed viable alternate structural system
Non-composite deck + K-series joists + girders
Controlled lateral deflections
Decreased eccentricity
Reduced project costs + schedule
Impacted Architecture Positively
Eliminated bracing
Increased Fireproofing Options

## Slide 27
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Acknowledgements
VCU SOM
Gilbane Building Company {MARO}
Nick Ivey
Virginia Commonwealth University
Entire PSU AE Faculty
Professor Linda Hanagan
Professor M. Kevin Parfitt
Family & Friends

## Slide 28
Project Overview
Proposal
Gravity System
Redesign
Vibration Control
Lateral System
Moment Frame Layout
RAM Model
Cost & Schedule Analysis
Architectural Impacts
Conclusions
Comments
VCU SOM