## Slide 1
Aria Health | Torresdale Campus
Emergency Department | Expansion
Robert M. Stano | AE | Construction Option
Adviser | Dr. Chimay Anumba
Senior Thesis Presentation | April 16th, 2014

## Slide 2
Bob Stano | Construction
Project Summary
Aria Health | Torresdale Campus | ED Expansion
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Overall Theme
Analysis 1 – Rainwater Collection
Analysis 2 – Photovoltaic Array
Analysis 3 – Operable Solar Shading
Analysis 4 – Modularization of Patient Treatment Rooms (not presented)
Sustainable Construction

## Slide 3
Bob Stano | Construction
Project Summary
Location: Philadelphia, PA
Building Information:
2 Stories Above Grade, 1 Below
Structural Steel
80,000 SF
Emergency Department Addition and Renovation
Construction:
$35 MM
2/25/13 – 6/27/14
CM at Risk
GMP Contract
Owner: Aria Health Systems
Owner’s Representative: Stantec
Architect: Francis Cauffman
MEP Design: PWI
Structural Design: O’Donnell & Naccarato
Civil Design: Barry Isett & Associates
Construction Manager: Turner Construction Company
Aria Health | Torresdale Campus | ED Expansion
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 4
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 1 – Rainwater Collection
Analysis Goals
Data Collection
Data Collection
Primary: To show how sustainable construction techniques can be used for the purpose of resource conservation.
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 5
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 1 – Rainwater Collection
Description
Design
Design
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
85 GPM
Submersible

## Slide 6
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 1 – Rainwater Collection
Cost Estimate
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 7
Bob Stano | Construction
Analysis 1 - Rainwater Collection
Aria Health | Torresdale Campus | ED Expansion
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 8
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 2 – Photovoltaic Array
Analysis Goals
Data Collection
Data Collection
Primary: To show how sustainable construction techniques can be used for the self-production of electricity.
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 9
Bob Stano | Construction
Analysis 2 - Photovoltaic Array
Sharp ND-F4Q300
Schletter VarioTop Racking System
Aurora PVI-12.0-I
Inverter
Aria Health | Torresdale Campus | ED Expansion
Description & Design
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
10.8 kW Produced

## Slide 10
Bob Stano | Construction
Analysis 2 – Photovoltaic Array
Parallel Feeder
Series Branch
Direct Current
Alternating Current
Aria Health | Torresdale Campus | ED Expansion
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 11
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 2 – Photovoltaic Array
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 12
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 2 – Photovoltaic Array
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 13
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 3 – Operable Solar Shading
Primary:
To show how sustainable construction techniques can be used for the purpose of annual energy savings.
Analysis Goals
Design and Prefabrication
  Mestek’s Linel Fabrication
Automation
  Preprogrammed Weather Data
Contractual Agreements
  Lump Sum Quote
Procurement and Logistics
  16-20 Week Lead
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Description
Description

## Slide 14
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Analysis 3 – Operable Solar Shading

## Slide 15
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 3 – Operable Solar Shading
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 16
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Analysis 3 – Operable Solar Shading
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 17
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Thesis Recap and Recommendations
Analysis 1 – Rainwater Collection
Analysis 2 – Photovoltaic Array
Analysis 3 – Operable Solar Shading
Initial Cost: $146,680.40
Payback: 12.18 Years
Cumulative Income: $281,105.50
Recommended
Initial Cost: $211,958.98
Payback: 19.52 Years
Cumulative Income: $94.467.20
NOT Recommended
Initial Cost: $442,533.33
Energy Savings: 20% Reduction in cooling load
Cost Savings: $935.97 savings per year
NOT Recommended
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 18
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Acknowledgements
Adviser:
Dr. Chimay Anumba, FREng., Ph.D., D.Sc., Dr.h.c., P.E.
Project Team:
Patrick F. Kershner, Project Manager
Michael Zarzycki, Superintendent
Tolulope A. Adenubi, Project Engineer
Very Special Thanks:
Robert F. Stano, P.E.
Steven P. Mulhollen, P.E.
John C. Stewart, P.E.
Scott A. Mack, P.E.
Gregory D. Rummel, CPD
Cordell A. Adamy
Andrew Rhodes, P.E., DBIA, LEED BD+C
Francis O’Neill
Ted Border
Nicholas M. Rekstad
Kevin A. Martyn
Friends and Family
The Pennsylvania State University
Architectural Engineering
Faculty and Staff
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements

## Slide 19
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Thank You
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Questions?

## Slide 20
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Appendix – Rainwater Collection
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Pump Sizing – Fixture Units
10 fixture units per water closet
5 fixture units per urinal
Cross referenced with the hunter curve to find 85 GPM
Pipe Wheel used for pipe sizing
Hydro Pneumatic Tank Sizing
Worked backwards….
Assume 850 Gal, or 2/3 capacity is available before booster pump kicks on.
for
Rainwater Economic Analysis
Maintenance: 16 hours/day at union plumber wage of $59.68/hour
General Inflation = 3% per year
Utility Inflation = 5% per year

## Slide 21
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Appendix – Photovoltaic Array
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Photovoltaic Economic Analysis
Maintenance: 16 hours/day at union electrician wage of $110.64/hour
General Inflation = 3% per year
Utility Inflation = 5% per year
Solar Renewable Energy Credits
It is assumed that SREC’s will DEFLATE by 5% per year for ten years, after which SREC’s will no longer exist.
ABB: Protecting and Isolating PV Systems

## Slide 22
Bob Stano | Construction
Aria Health | Torresdale Campus | ED Expansion
Appendix – Solar Shading
Project Summary
Analysis 1: Rainwater Collection
Analysis Goals
Data Collection
Description & Design
Cost Estimation
Economic Analysis
Analysis 2: Photovoltaic Array
Analysis Goals
Data Collection
Description & Design
Electrical Breadth
System Layout & Cost Estimation
Economic Analysis
Analysis 3: Operable Solar Shading
Analysis Goals
Colt Shadoglass
Cost Estimation
Sequencing, Schedule, Logistics
Energy Model
Mechanical Breadth
Thesis Recap
Acknowledgements
Industry Standard Value