## Slide 1: 8621 Georgia Avenue Silver Spring, MD
By: Nick Dastalfo
Structural Option
Advisor: Dr. Boothby

## Slide 2: Site Conditions
Location
Existing Site

## Slide 3: General Building Information
Owner: Foulger-Pratt Development, LLC
Number of Stories: 17 stories, 161 ft.
Size: 347,009 ft.²
Cost: $51 Million
Structural Engineer: Holbert Apple Associates
Construction: Beginning in 2015
Unique Features: Green Roof, Rooftop Pool

## Slide 4: Existing Structural System
Gravity System:
  Columns vary in concrete strength
  Mild-reinforced two way slab with drop panels
  Post-tensioned two way flat slab
    7.25” depth, banded and distributed tendons
Lateral System:
  Concrete shear walls
  Concrete Moment frames
Foundation:
  Spread Footings

## Slide 5
Typical Bay

## Slide 6: Typical Bay
7.25” post-tensioned slab
Columns: 16” x 24”
Banded and distributed tendons
24’-0”
20’-0”

## Slide 7: Gravity Spot Checks -Punching Shear
Punching Shear - Int. Column C6
  ΦVc117.65k > Vu=93.1k
Punching Shear – Ext. Column C1
  ΦVc103.04k > Vu=55.2k

## Slide 8: Gravity Spot Checks -One Way Shear
22’-0” Direction
  H=7.25”
  ΦVc = 152.3k > Vu = 78.5k
20’-2” Direction
  H=7.25”
  ΦVc = 139.5k > Vu = 79.8k
C6
22’-0”
20’-2”

## Slide 9: Gravity Spot Checks -Moment Capacity
Deflection Control
  0.317” < 0.8”
Load balancing

## Slide 10: Design Alternates
Alternate #1: Two Way Flat Plate Slab
Alternate #2: Composite Steel
Alternate #3: Non-Composite Steel

## Slide 11: Two Way Flat Plate Slab
Notes:
  Thickness = 9”
  Rebar fy=60ksi, Concrete f’c= 5ksi
  No drop panels

## Slide 12: Two Way Flat Plate Slab
Depth
  Slight increase from 7.25” to 9”
Fire
  Meets at least 2 hr requirement
  No additional fire-proofing
Weight = 115 psf
Cost
  $19.84/SF
  $0.32 savings per SF
Lateral Options
  Concrete SW and MF
Conclusion
  Heaviest
  Limited depth
  Viable Option

## Slide 13: Composite Steel
Notes:
  Deck= 2VLI18, 5in. NW Concrete topping
  Shoring Required
24’-0”
20’-0”

## Slide 14: Composite Steel
Depth
  Increase from 7.25” to 21”
Fire
  Meets 2 hr requirement with 3.5” topping
  Fire-proofing needed on beams and deck
Weight = 75 psf
Cost
  $18.48/SF
  Cheapest
Lateral Options
  Concrete SW or Steel MF
Conclusion
  Very Deep
  Shoring
  Viable but not efficient

## Slide 15: Non-Composite Steel
Notes:
  Deck= 1.5C18 3.5” NW Concrete Topping
24’-0”
20’-0”

## Slide 16: Non-Composite Steel
Depth
  Increase from 7.25” to 21.5”
Fire
  Meets 2 hr requirement with 5” topping
  Fire-proofing needed on beams and deck
Weight = 60 psf
Cost
  $27.60/SF
  Most expensive
Lateral Options
  Concrete SW and MF
Conclusion
  Lightest
  Very Deep
  Viable Option

## Slide 17
Final Comparison

## Slide 18: Thank You!
Questions?